## Slide 1: Lecture 2b
Protocol Layers – The OSI and TCP/IP Models

## Slide 2: Last Class
Circuit Switching Vs Packet Switching
Protocols
Layers

## Slide 3: Why protocol?
Allow different devices to communicate
For example: you go to the store and buy a phone from one of a dozen different vendors. When you get home and plug in the phone to the same cable in which your old phone was connected, the new phone works. The phone vendors know the standards for phones in their country and build their phones to match those standards.
Similarly, when you buy a new computer, it implements the TCP/IP model to the point that you can usually take the computer out of the box, plug in all the right cables, turn it on, and it connects to the network.
How? The OS on the computer implements parts of the TCP/IP model. The Ethernet card, or wireless LAN card, built in to the computer implements some LAN standards referenced by the TCP/IP model. In short, the vendors that created the hardward and software implemented TCP/IP.

## Slide 4: History Leading to TCP/IP
Vendors created the first networking protocols, such as IBM Systems Network Architecture (SNA) in 1974
Vendor-neutral networking model would aid competition and reduce complexity. The International organization for Standardization (ISO) took on the task to create Open Systems Interconnection (OSI) model in 1970’s.
DoD and researchers at various universities volunteered to help develop a competing open network model called TCP/IP in 1990’s
Here, in the twenty-first century, TCP/IP dominates.

## Slide 5: Revisiting Greeting Card Scenario
Alice writes greeting card to grandmom
Grandmom reads greeting card
Alice puts it in envelope
Grandmom removes from envelope
Alice drops envelope in mailbox
Grandmom retrieves envelope from mail
Mailman picks up the mail from box
Mailman delivers mail to mailbox
Truck carries mail to post office
Truck carries mail from post office
Mail gets sorted
Mail gets sorted
Transport
There is a one-to-one correspondence
between layers in the two end points
There is a structured “flow”
between layers at each end

## Slide 6: Layering in packet switched networks
Alice wants to browse Amazon.com
What happens next?
Applications
Protocol Stack
Application
(Process)
TCP
Socket

## Slide 7: Simplified Web Browsing
Message from Alice’s Browser
Web server process gets message
TCP Segments Created
TCP segment is recovered, assembled
IP datagrams carry TCP segments
IP datagram is picked up from frame
Ethernet in Alice’s PC creates frame
Ethernet in server gets frame, checks for errors
Ethernet cable carries signal to edge router
Cable carries the signal representing Ethernet frame to server machine
Ethernet in router gets frame , checked for errors
Puts it in Ethernet frame
Transport
There is a one-to-one correspondence
between layers in the two end points
There is a structured “flow”
between layers at each end
Looks at IP DA for routing
Edge router receives IP datagram
Notes: Same layer interaction on different computers, adjacent-layer interaction on the same computer

## Slide 8: TCP/IP Application Layer
Provide services to the application software running on a computer.
Notes: The application layer does not define the application itself, but it defines services that applications need.
For example, you may have different web browsers like chrome, safari, firefox, etc. All of them use Hypertext Transfer Protocol (HTTP).

## Slide 9: TCP/IP Transport Layer
Provide services to the application layer protocols: reliable end-to-end transmission
Transmission Control Protocol (TCP) and User Datagram Protocol (UDP)
How about the request that send from the client is lost?

## Slide 10: TCP/IP Network Layer
Provides addressing and routing (Postal service)
Internet Protocol (IP)
IP defines each host computer should have a different IP address, just as the postal service defines addressing that allows unique addresses for each house, apartment, and business.

## Slide 11: TCP/IP Network Layer
Simple TCP/IP network: three routers with IP addresses grouped
How to send?

## Slide 12: TCP/IP Data Link Layer
Deliver data across some physical network
Ethernet

## Slide 13: TCP/IP Physical Layer
Medium
Signal

## Slide 14: Internet Protocol stack
Five layer stack built around Internet Protocol (IP) from IETF
Note multiple layer 1-2, and 5 protocols
Slide modified from Agrawal
Example technologies

## Slide 15: Packet structure influenced by communication needs
Five important communications tasks
  User commands, responses
    Example: get web page, web page body
  Segmentation and reassembly
    Cannot send whole web page in a TCP segment (it is too big), we have to send it in pieces
  Identifying and locating destination
    We guessed the IP destination address may be in the IP header
  Error control
    What happens if some bits are flipped?
  Signaling
    Converting data into a form suitable for transmission over wires
Slide modified from Agrawal

## Slide 16: Header information
The previous slide’s communication and other related datacomm tasks are accomplished by adding additional required information to information packets
  Packet header
    Organized in a layered structure
  Routers and end stations use this header information to handle packets appropriately
    The router that connects Alice’s network to the Internet is the “receiver”
Again: Routers perform packet switching
Slide modified from Agrawal

## Slide 17: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
Slide modified from Kurose-Ross
Uses “link or MAC address” at frame level
Alice
Bob
Uses “IP address” at datagram/network level
Signal

## Slide 18: Typical packet structure
A typical packet contains
  Information sent from the layers above
  and
    Additional information (called headers) specific to the functions of each layer
    At a high level, looks like this:
Slide modified from Agrawal

## Slide 19: More Questions
What is the structure of the TCP segment? How many bits? Is it fixed? What does the TCP header contain? Why?
What does the IP header contain?
  One guess is it has Amazon.com’s IP address as the destination address
Who is the receiver of the Ethernet frame? And what does this receiver do with the embedded IP datagram?
  Does the receiver look at the TCP segment within the IP datagram?
  How about the commands, responses, and data from the application?

## Slide 20: Simplified View of Web Browsing (1)
Assume that Alice’s computer knows the IP address of amazon.com say 205.251.242.54
A TCP “segment” is created which is passed on to the so-called “network layer”
The TCP segment becomes the payload of an IP packet or datagram
All of this happens in the OS of Alice’s computer
TCP Header
TCP Payload
TCP segment
IP Header
IP Payload
IP Datagram
Note that the TCP segment and the IP datagram are simply groups of bits with some structure
Application
(Process)
TCP
Socket
IP

## Slide 21: Simplified View of Web Browsing (2)
The process continues
  IP datagram becomes the payload of the link/MAC layer “frame”
  Say Ethernet frame
PHY Layer
  The Ethernet frame is converted into a set of electrical pulses (signal) that is placed on the Ethernet cable
  The signal is picked up by a receiver
  Who is the receiver?
Application
(Process)
TCP
Socket
IP
Ethernet
PHY
5. Application
4. Transport
Socket
3. Network
2. Link/MAC
1. Physical

## Slide 22: Layer names and tasks
Layer number | Layer name | Networking task | Header information
5 | Application | Specify user needs, creates “message” | User commands
4 | Transport | Segmentation and reassembly of data “segments”, sometimes reliable transfer & speed matching | Sequence numbers
3 | Network | Identifying and locating destination, best effort delivery of “datagrams” | Address
2 | Data-link | Reliable delivery of “frames” over a link, Error control | Error check
1 | Physical | Signaling, moving individual bits based on medium | Usually none, but in WiFi there is a header
Slide modified from Agrawal

## Slide 23: Internet stack technologies by layer
This is not an exhaustive list, but shows some of the most popular technologies at each layer
We will look at the details of some of them over the span of the semester
Slide modified from Agrawal

## Slide 24: OSI model
OSI – Open Systems Interconnection
Early packet switched networks involved multiple networking technologies
  SNA, DECnet, Netware, Ethernet, Appletalk
  Created communication islands
  Strong need to ensure inter-operability
OSI model is a logical structure for communications networks, standardized by the International Organization for Standardization (ISO)
  An effort by the ISO to standardize computer networks
  ISO 7498: 1984
  All network traffic can be processed in a cookie-cutter manner by routers, irrespective of application
Slide modified from Agrawal

## Slide 25: OSI model
OSI model useful frame of reference
Current wired networks built around Internet protocol stack
Slide modified from Agrawal

## Slide 26: OSI and TCP/ IP
Presentation
  Allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
Session
  Synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  These services, if needed, must be implemented in application
Slide modified from Agrawal, Kurose & Ross

## Slide 27: Internet

## Slide 28: Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  Residential, company and university ISPs
Access ISPs in turn must be interconnected.
  So that any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies
We take a stepwise approach to describe current Internet structure
Slide modified from Kurose & Ross

## Slide 29: Simplified Internet Structure
Hierarchical
  Revisit at the end of the lecture
Access network has a router that connects it to a regional ISP
Regional ISPs connect to global ISPs
Remember: Router = packet switch
Transport
mobile network
global ISP
regional ISP
home
network
institutional
network
Figure from Kurose-Ross

## Slide 30: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Slide modified from Kurose & Ross

## Slide 31
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
Slide modified from Kurose & Ross

## Slide 32
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP
Slide modified from Kurose & Ross

## Slide 33
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C
Slide modified from Kurose & Ross

## Slide 34
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point
Slide modified from Kurose & Ross

## Slide 35
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
IXP
regional net
Slide modified from Kurose & Ross

## Slide 36
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network
Slide modified from Kurose & Ross

## Slide 37
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP
Slide modified from Kurose & Ross

## Slide 38: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence
Slide modified from Kurose & Ross

## Slide 39: Net Neutrality
Have you heard the news…
https://www.youtube.com/watch?v=l9jHOn0EW8U