## Slide 1: Lecture 4a
Signaling

## Slide 2: So far …
Big picture
Layers
Transmission media
Signals
  Analog
  Digital
  Sinusoid

## Slide 3: What is signaling?
Mac OS X Dictionary
  “transmit information or instructions by means of a gesture, action, or sound”
Two primary approaches
  Baseband analog or digital
    Voice on copper cable in landlines
    Bits in Ethernet on coaxial or UTP
  Bandpass analog or digital
    AM/FM radio, Cellular Telephone Signals, Coaxial cable TV

## Slide 4: Origins of signals
Analog signals come from sensors of various kinds (e.g., microphones)
Digital signals come from computers and digital devices of various kinds
Question: Do you type in binary?

## Slide 5: Source Encoding
Problem: how can we represent alphanumeric characters in bits?
Solution:
  Create a mapping between the alphanumeric characters and bits
    Object set  Code set
    Easier since the set is finite and known
What are design objectives of a code?
How do we encode “analog” data or signals?

## Slide 6: Examples of Source Encoding
Object set
  Alphanumeric characters
    a-z
    A-Z
    0-9
  Special characters (`~!@#$%^&*()-_=+\|{[}}:;””,<.>/?)
  Control characters
Code set
  {0,1} for binary codes
  Can be anything in principle
Code types
  Length
    Fixed (e.g., ASCII)
    Variable (e.g., Morse)

## Slide 7: ASCII
Design objectives
  Universal code for all computers
  Unambiguous interpretation of received information by dumb receivers
Standard Code Developed by the American National Standards Institute (ANSI)
  Seven bit code (fixed)
  Stateless (each object is encoded independently)
Object set
  Upper and lower case alphabet
  Numbers
  Selected keyboard characters
  Control characters
American Standard Code for Information Interchange

## Slide 8: Examples in ASCII
Jones
Transmission Direction
J
0111010
1101111
1101110
1100101
1110011
o
n
e
s
A12B3C7
Transmission Direction
A
1000001
0110001
0110010
1
2
B
1000010
0110011
1000011
3
C
0110111
7
Notes: The transmission direction is important because it clarifies the high order bits from the low order bits. From the ASCII table, bit 7 is transmitted first. Transmission is normally from the high order bit to the low order bit, although it can go both ways.

## Slide 9: Local Loop in Landlines
The local loop carries an “analog” baseband voice signal
  Created by microphone
  Carried on phone wire (copper)
The human ear can perceive frequencies from 20 Hz up to 20 kHz
  Voice has “energy” content primarily between 50 Hz and 3400 Hz
  The local loop cable and filters truncate the bandwidth to roughly 3500 Hz
…
…
Central
Office

## Slide 10: Why Use Analog Transmission?
In place in legacy systems
  Sufficient for transmission of voice signals
  Or any natural signal that is inherently analog
Significantly less expensive
  At the end-point, but not the network
Some transmission media best suited to propagate analog signals
  Unguided media (air)
  Used in digital cell phones, radio, TV

## Slide 11: Why Digital?
Technology
  Convergence of computing and communications
  MUXs, decoders etc.
Integration
  Voice, video, audio all on the same infrastructure
Regeneration
  Amplifiers Vs Repeaters
Multiplexing
  In time is easy, also in code
Encoding
  Most significant advantage
Monitoring/control
  Performance tweaking, alarms, etc.
Standardization
  Easy to define interfaces
  Interoperability

## Slide 12: Analog to Digital Transmission
Permits use of digital transmission and switching equipment
  Unified communications (treat everything as bits)
Analog signal must be encoded for transmission – termed CoDec (coder/decoder)
  Encoding implies conversion to a digital format
Source Coding – more efficient encoding to improve quality or reduce bit rate – vocoder ITU G.729, MPEG video coders

## Slide 13: Analog to Digital
Common approach
  Sample the analog signal
  Signal must be sampled at least at a rate that is twice the maximum frequency component of the signal (Nyquist’s Theorem)
  Quantize the samples into a finite number of levels
  Assign a set of bits to each level
    Bits/sample

## Slide 14: Quantization - I
Idea
  Suppose the samples of the continuous-time signal are {…, -1.01, 0.83, 0.38, 1.27, … }
  We convert them to something like {…, -1, 0.8, 0.4, 1.3, …}
  Or we convert them to {…, -1, 1, 0, 1, …}
Which has higher errors?
  Error = exact value - approximation
The error samples are {…, -0.01, 0.03, -0.02, 0.03,…} or {…, -0.01, -0.17, 0.38, 0.27, …}
sublime
impressive
Quantization
Wow!

## Slide 15: Quantization - II
Let the highest analog value be H
Let the lowest analog value be L
We will divide the range (H-L) into N intervals each of size s
  So s = (H-L)/N or Ns = (H - L)
  Find the midpoint of each interval
H
H - s
H - 2s
L
L + s
…
…
H - s/2

## Slide 16: Quantization - III
Determine where the analog sample lies
  Example: Analog value is H - 0.37s
  It lies in the interval H - 0.3s and H - 0.4s
Replace the analog value by the midpoint of the interval
  Example: Replace H - 0.37s by H - 0.35s
Companding
  Compress levels at smaller values, expand levels at higher values

## Slide 17: Quantization Example

## Slide 18: Why not digital?
Conversion
  Where, how and when to convert?
Bandwidth
  A 4 kHz voice signal needs 64kbps as a digital signal
    See next slide
Delay
  Processing of digital signals is easy, but it adds to delays
Synchronization
  Where does a bit start? Where does it end?
Quantization noise
Non-linearity of digital signals

## Slide 19: Pulse Code Modulation (PCM)
The conversion of a quantized signal into bits is essentially what we call as “pulse code modulation” or PCM
  We use n-bits to represent the samples
  Each group of n bits is called a codeword
Example: Analog voice
  Sampled 8000 times/second
  Either 128 or 256 levels to represent each sample
  256 levels = 8 bits => bit rate = 64 kbps
  This is the DS0 format

## Slide 20: Line Coding
Representing a digital value by an analog signal
  Modulation includes a carrier (recall fc)
Unipolar return-to-zero (RZ) and unipolar non-return to zero
t
0
0
0
0
0
1
1
1
T
2T
t
0
0
0
0
0
1
1
1
T
2T
How many zeros?

## Slide 21: Line Codes
Non Return-to-Zero (NRZ)
  Each digital value is represented by a voltage pulse
  The voltage value is constant for the entire symbol duration
Return-to-Zero (RZ)
  Voltage pulses have duty cycles
    They do not last for the entire symbol duration
    If the duty cycle is 100%, it becomes NRZ
Unipolar
  Signal values are 0V or some positive voltage
Antipodal (or bipolar)
  Both positive and negative voltage values (usually identical in magnitude) exist

## Slide 22: Comparison of Four Combinations
Combinations
  Unipolar RZ, NRZ and Bipolar RZ, NRZ
  Assume RZ has 50% duty cycle
Signal Power
  Peak and average
Bandwidth
  RZ needs more bandwidth (why?)
Sampling threshold for discrimination
  Antipodal has a zero threshold for binary
Transitions
  RZ has more transitions, but no difference between unipolar and antipodal
Bandwidth of a rectangular pulse
Pulse train
Pulse
Spectrum

## Slide 23: Manchester Code
Used in Ethernet
Signal power
  Same as NRZ
Bandwidth
  Twice (like RZ)
Transitions
0
1

## Slide 24: Carrier Modulation
Impressing data on a carrier wave (sinusoid)
The data are contained in some parameters of a sinusoid given by
c(t) = A cos(2πfc t + φ)
The original data signal is called the baseband signal
Modulation moves the spectrum of the signal to a region around fc
  We say that the modulated signal is a bandpass signal
Parameters: amplitude A, frequency fc and phase φ
Baseband
Bandpass
LSB = Lower Side Band, USB= Upper Side Band

## Slide 25: Why Modulation?
Medium characteristics
  Using strictly baseband analog or digital signals is not practical
Radio transmissions
  Antenna sizes are smaller as fc increases
Simplifying circuitry
  Use of a single intermediate frequency enables us to make best use of hardware components
Multiplexing

## Slide 26: Analog Modulation
The amplitude, frequency or phase changes continuously as a function of the baseband signal
AM – Amplitude Modulation
  525 – 1715 kHz, Bandwidth = 10 kHz
  KDKA
FM – Frequency Modulation
  88 MHz – 108 MHz
  Bandwidth = 200 kHz
Show AM in Matlab or R

## Slide 27: AM Example
Different types of AM exist
Notice that the carrier’s “envelope” is changing
Underneath, we still have a sinusoid

## Slide 28: Digital Modulation
The amplitude, frequency or phase change in a discrete manner following the baseband signal
  Called amplitude, frequency or phase shift keying (ASK, FSK, PSK)
Discrete symbols represented by specific continuous-time signals lasting for Ts seconds
  Symbol rate = 1/Ts
Binary: One bit per symbol for a total of two different symbols and signals
  Symbol rate = bit (data) rate = 1/Ts
M-ary: k bits per symbol for a total of 2k = M different symbols and signals
  Symbol rate = 1/Ts; Bit (data) rate = k/Ts
  Symbol rate is also called baud

## Slide 29: Binary ASK or On-Off Keying
Historically:
  Morse code on RF carriers
Today: Photonics, RF-ID tags, television remotes, IR links
How do we write s(t)?

## Slide 30: BFSK
Use two different frequencies to represent “0” and “1” Signals are given by:
si(t)=A cos(2πfit), 0≤t ≤Ts for i =1,2
Send s1(t) if the bit is zero, send s2(t) if the bit is one
Signaling in analog (1G) cellular telephones
Bluetooth, Zigbee and sensor networks

## Slide 31: BPSK
Use two phases to represent “0” and “1” Signals are given by:
si(t)=A cos(2πfct+φi), 0≤t≤Ts for i=1,2
Send s1(t) if the bit is zero, send s2(t) if the bit is one
It is common to assume that φ1 = 0 and φ2 = π
BPSK is equivalent to antipodal signaling with non-return-to-zero (NRZ) pulses
The transmitter can be simply implemented as a multiplication of the baseband antipodal signal and the carrier at frequency fc

## Slide 32: M-Ary Modulation
Quadri-phase Shift Keying (QPSK) uses 4 phases
  Each symbol carries 2 bits
Quadrature Amplitude Modulation (QAM) uses both amplitude and phase of a carrier to encode information
  Example: 16-QAM symbols carry 4 bits
QPSK and QAM are common in wireless networks
  QAM also used widely in cable modems, DSL and dial-up

## Slide 33: Signal Constellation
Representation of signals used for communications in a graphical manner
Shows the “distance” between signals
  Larger the distance, easier it is for the receiver to distinguish between the signals
More signals => smaller distance for the same power
  Error rates

## Slide 34: QPSK

## Slide 35: 8 QAM

## Slide 36: Next
Impairments
  Noise, Attenuation, Channel Bandwidth
Error rates and error control coding
Multiplexing