## Slide 1: Lecture 5a
Communication Impairments
Noise, Loss, and Delay

## Slide 2: So far…
Signaling
  Line codes
Modulation
  Analog and Digital
Next
  Noise, Attenuation, Delay

## Slide 3: Noise
Noise is any undesirable signal that impacts the quality of a desired signal
  Example: Static or crackle in analog audio
  Example: Snow in analog video transmission
  Example: Bit errors in digital transmission

## Slide 4: Communications Impairments
Analog signals and systems have various impairments that affect the signal
Important ones that warrant detailed treatment
  Noise
  Loss
  Delay
Others include cross-talk, reflection, dispersion, and distortions

## Slide 5: Analog signals and noise
Imagine trying to speak when a vacuum cleaner is running
  You have to shout on top of the “noise” that it makes
    Increase the “power” in your voice and thus the signal-to-noise ratio
  The noise “adds” to your speaking
In telecommunication networks noise comes from
  Electromagnetic interference (EMI)
  System processing

## Slide 6: Noise and Distance
Signals get weaker over distance
  But noise keeps getting added up
  Eventually the noise becomes too loud to receive the signal
Try tuning in to your favorite radio station about 50 miles from your city
Notes: Lightning discharges
Interfering transmissions from other communications equipment
Solar flares
Emissions from space
Lawnmowers and hairdryers
Microwave ovens

## Slide 7: Additive White Gaussian Noise (AWGN)
White Noise
  Background or thermal noise
    Due to random fluctuations of electrons - function of absolute temperature
Adds to the signal
  Most noise adds to the signal, but some multiply with the signal
Ideal case
  There will always be AWGN, but hopefully that is all there is
Notes: As I mentioned earlier, Shannon-Hartley is the reason for the additional capacity of STP vs. UTP. Essentially, the shielding reduces noise on the signal, which increases the SNR, which, in turn, increases capacity.

## Slide 8
Questions
  What is signal quality?
  How does noise impact signal quality?

## Slide 9: Impact of noise on digital signals
The received signal can get seriously affected by noise
The receiver has to be able to interpret the result correctly for reliable data transmission
Chart: Transmitted signal
Chart: Received signal

## Slide 10: Signal-to-Noise Ratio
Measure of “quality” of the received signal
Ratio of the signal power to noise power at a receiver SNR = S/N where S and N in watts (W) or milliwatts (mW)
SNRdB = 10 log10 (S/N) in decibels (dB)
  What is dB?
High SNR
Low SNR

## Slide 11: Eye Diagram
Oscilloscope trace of 14 4-bit binary signals
  Middle two bits overlapped on a single display
Demonstrates issues with digital signals
  Note “eye”
  Cursive Vs print

## Slide 12: Observations
Attenuation through channels close the “eye”
Detecting bits involves sampling
  Sampling => need to find the sweet spot
Dispersion and inter-symbol interference (ISI)
All impact bit error rates
  What fraction of detected bits are in error?

## Slide 13: Noise and Eye Diagram
The eye is closed more!
Attenuation lowers the upper eyelid and raises the lower eyelid
Noise blurs the distinction between the two
Signal-to-noise ratio!

## Slide 14: Review of Logarithms
General Properties
  log (a×b) = log (a) + log (b)
  log (a/b) = log(a) – log(b)
  logn(n) = 1
  nlogn(x) = x
  logn(x)=log10(x)/log10(n)
Review: http://www.khanacademy.org/math/algebra/logarithms-tutorial

## Slide 15: Measuring Power: Decibels
Relative power ratios (signal strength ratios) are expressed in decibels (dB) for ease of calculation
10 log10(ratio)
  Ratio has no units
Example: A cell phone receives a signal with average power of 4 W and noise power of 0.5 W what is the SNR in dB?
  SNRdB = 10 log10 (S/N) = 10 log10 (4/0.5) = 9.03 dB

## Slide 16: dB Scale (2)
It is a logarithmic scale – “decibel”
  Used extensively in Telecom – simplifies math
  Multiplication becomes addition, exponentiation becomes multiplication
It is a “relative measure” – dimensionless arguments to the log
  Always need a baseline - for a general baseline, the unit is dB
  It measures energy or power, not voltage or current
  The power at point A PA is greater than the power at point B PB by X dB, if 10 log10(PA/PB) = X
The reason for multiplying it by 10 is that this is “deci” bels, not bels

## Slide 17: dB Calculations (1)

## Slide 18: dB Calculations (2)

## Slide 19: Absolute values in dB
If we have a transmitter sending a signal with transmit power x W, how can we represent this in dB?
  Use some known quantities as a reference
  Typically, we use 1 mW or 1 W as the reference
  If the reference is 1 mW, the actual value is expressed in dBm
  If the reference is 1 W, the actual value is expressed in dBW
Example:
  If the transmit power is 100 mW, in dBm, it is
10 log(100 mW/1mW) = 10 log(100) = 20 dBm
or in dBW, it is
10 log(100 mW/1W) = 10 log(0.1) = −10 dBW

## Slide 20: Loss
Two problems of “Tele”communications
  Deliver signal to many destinations
  Destinations are far away ⇒ Loss of signal power between transmitter and receiver
Two types of losses
  Dissipation – energy gets scattered in many directions and loses intensity
  Attenuation – energy is absorbed (maybe converted to heat) and thus losses intensity

## Slide 21: Dissipation
Consider a light bulb that emits light at intensity Pt = 125.6 W
At a distance r from the bulb, the intensity is distributed over a sphere of radius r and area 4πr2
  The density of intensity is Pt/4πr2 = 10/r2 W/m2
Let us suppose that the “receiver” is a sheet of paper of area 1 m2
What is the total intensity Pr received by the paper at different distances?
  At r = 5m, Pr =10/25 = 0.4 W
  At r = 10m, Pr =10/100 = 0.1 W
As the distance doubles, the received intensity falls by ¼
We say the signal power has dissipated as Pr = k Pt/r2 where k is a constant

## Slide 22: Attenuation
A foggy room with a light bulb (or a laser)
  Light intensity drops even if it did not spread
  Absorption of energy by fog causes “attenuation”
Telecommunications example
  We want to make the time-varying voltage at point A known at point B
  Suppose we connected the two points by a wire
  The energy in the signal at A will be larger than the energy of the signal at B
Why?
  Not because the energy is spread in space
  The energy is lost as heat or absorbed along the wire
  It is like “friction” – the lost heat cannot be usefully employed

## Slide 23: dB Example (1)
Let the signal power at the input of an optical link be P1 = 0.1 W
Let the signal power at the output of the optical link be P2 = 0.05 W
We will say that “P2 is 3 dB smaller than P1” because
  10 log10 P2/P1 = 10 log10(1/2) ≈ −3dB
So if the power in a signal gets reduced by half every km, we will say
  The attenuation loss is 3 dB per km

## Slide 24: Copper Wire Example
3

## Slide 25: Optical Fiber Example

## Slide 26: Radio Link Example

## Slide 27: Link Power Budget
Balance sheet of gains and losses in a system
Allows you to determine
  Coverage of your communication link
  How far can the signals go?
  Transmit power
  Receiver capability
Different components for different systems
  Optical Vs Copper Vs Wireless

## Slide 28: Basic Concept of Link Budget

## Slide 29: Link Budget—Transmit Power
The distance between transmitter and receiver is 6 km, the loss factor is 3 dB per km. At the receiver side, the noise level is 3 dBm. The received signal power needs to be twice as large as noise in order for receiver to differentiate the signal from noise. What is the minimum transmission power level?

## Slide 30: Link Budget –Maximum transmission Distance
The transmission power is 20 dBm, it losses 3 dB per Km. The noise level increase 1 dB per Km. Receivers require the SNR to be 3 dB. What is the maximum transmission distance on this line?

## Slide 31: Delay
Not significant in single link one-way broadcast
Has cognitive impact in interactive communications
Causes
  Transmission, queueing, propagation, processing
Finite velocity of signals in media
  Capacitive and inductive effects slow down signals
  Depending on cable, the speed is 5% to 75% of the speed of light
What is the delay between LA and Boston (4800 km) if the speed of transmission on a copper link is 0.2c?

## Slide 32
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Sources of Delay
Notes: 32

## Slide 33: Processing Delay
The time required to examine the packet’s header and determine where to direct the packet.
Other factors: time needed to check for bit-level errors
Processing delays in high-speed routers are typically on the order of microseconds or less.

## Slide 34: Queueing Delay
Packets queue in router buffers
  Packets arrival rate to link (temporarily) exceeds output link capacity
  Packet queue, wait for turn
  Arriving packets dropped (loss) of no free buffers
Factors that impact queueing delay
  Arrival:
    packet length (L) in bits
    average packet arrival rate (a)in packets per second
  Departure rate (R): link bandwidth in bps
  La/R determines the queue length

## Slide 35: Queueing Delay (cont’d)
La/R determines the queue length
  ~0: average queueing delay is small
  ->1: average queueing delay is large
  >1: more arrival than can be serviced, average delay increase to infinity
La/R ~ 0
La/R -> 1

## Slide 36: Transmission Delay
The amount of time required to push (transmit) all of the packet’s bits into the link.
Formula
  : the length of the packet in bits
  : transmission rate of the link in bits per second
Example
  We have a 1500 byte Ethernet packet being sent out on a 100 Mb/s link. What is transmission delay?

## Slide 37: Propagation Delay
The time required for any bit to travel on the link from node A to node B.
Formula
  : Distance between node A and node B in meter
  : propagation speed of the link in meter per second
Example
  We have a single optical fiber running from the east coast of the US to the west coast (around 5000 km). The propagation speed of the link is 2/3 of the speed of light. What is the propagation delay?

## Slide 38: Caravan Analogy
Cars “propagate” at 100 Km/hr
Toll booth takes 12 sec to service a car (bit transmission time)
Analogy: car ~ bit; caravan ~ packet
Question: How long until caravan is lined up before 2nd toll booth?
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 39: Caravan Analogy (cont’d)
Time to “push” entire caravan through tool booth onto highway = 12 sec/car * 10 cars = 120 sec
Time for a car to “propagate” from the 1st toll booth to the 2nd toll booth = 100 Km/(100Km/hr)=1hr
Answer = 120 sec + 1 hr = 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 40: Caravan Analogy (cont’d)
Suppose
  cars now “propagate” at 1000 Km/hr
  Toll booth now takes one minute to service a car
Question: Will cars arrive to 2nd booth before all cars serviced at first booth?
Answer: Yes! Why?
Animation
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 41: Real World Problem 1
There are two competing links between locations A and B separated by 1 km. The first uses fiber of length 10km over which the light signal propagates at 2/3 the speed of light. The transmission rate on the fiber link is 10Gbps. The second uses a UTP cable of length 1.5 km over which the electrical signal propagates at 0.7 times the speed of light. The transmission rate is 100 Mbps. If you wish transfer a 100 MByte file between A and B, which option would provide you the shortest overall delay? Assume the overall delay includes only the transmission delay and the propagation delay.

## Slide 42: Solution to Problem 1
Fiber
UTP
A
B
1 Km
Prop: 10 Km, 2/3 speed of light
1.5 Km
Prop: 1.5 Km, 0.7 speed of light
Tran: 100 MB, 10 Gbps
Tran: 100 MB, 100 Mbps
Fiber
UTP

## Slide 43: Real World Problem 2
Assume a 100Mbps link of 10,000 meters in length with 5 nanoseconds per meter propagation delay. Assume constant length 400 byte data frames, 64 byte ACK frames, 10 microsecond of processing delay for each data frame, and 5 microseconds of processing time for each ACK. The sender always has data to send. Solve for link utilization (U) between a sender and a receiver assuming a stop and wait protocol.
Utilization = transmission delay / total delay
How about ACK can be neglected?

## Slide 44: Solution to Problem 2
Utilization = transmission delay / total delay
How about ACK can be neglected?

## Slide 45: Real World Problem 3
Frames are generated at node A and sent to node C through node B. Determine the minimum transmission rate required between node B and C so that the buffers at node B are not flooded, based on the following:
  The data rate between A and B is 100 kbps
  The propagation delay is 5 milliseconds/Km for both lines
  There are full-duplex, error-free lines between the nodes
  All data frames are 1000 bits long; ACK frames are separate frames of negligible length
  Between A and B, a sliding-window protocol is used, with a window size of 3
  Between B and C, stop and wait is used.

## Slide 46: Solution to Problem 3 (1)
In order not to flood the buffers of B, the average number of frames entering and leaving B must be the same over a long interval.
Link A-B:
  Propagation delay = 4000 *5 µsec = 20 msec
  Transmission delay = 1000/(100*1000)=10 msec
Link B-C:
  Propagation delay = 1000 *5 µsec = 5 msec
  Transmission time per frame (x) = 1000/R
  R = data rate between link B and C

## Slide 47: Solution to Problem 3 (2)
A can transmit three frames to B and then must wait for the ACK of the first frame before transmitting additional frames. The first frame takes 10 msec to transmit; the last bit of the first frame arrives at B 20 msec after it was transmitted and therefore 30 msec after the frame transmission began. It will take an additional 20 msec for B’s ACK to return to A. Thurs, A can transmit three frames in 50 msec.
B can transmit one frame to C at a time. It takes 5+x msec for the frame to e received at C and an additional 5 msec for C’s ACK to return to B. Thus, B can transmit one frame every 10+x msec, or three frames every 30+3x msec.
Therefore, 30+30x=50, R=?

## Slide 48: “Real” Internet Delays
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes
3 probes

## Slide 49: “Real” Internet Delays
1 is the internet gateway on the network this traceroute was done from
2 is the ISP the origin computer is connected to
4-6-8. Pittsburgh-New York – Philadelphial
9 reach the edge router to wcupa