## Slide 1: Lecture 6a
(Coding) and Multiplexing

## Slide 2: Channel Capacity
Noise impacts the rate at which information can be sent of the channel
  Lumber on conveyor belt
  How do we best pack it?
Over simplified view in an AWGN channel
Capacity (C) = maximum rate in bps
  In bits per second
  Rate at which data is communicated over channel
Bandwidth (B)
  In cycles per second, or Hertz
  Constrained by transmitter and medium
SNR
http://www.hud-son.com/images/forestry-equipment/wood-conveyors/hud-son-wood-conveyor-c24b-01.jpg

## Slide 3: Channel Capacity
  Capacity in an additive white Gaussian Noise channel
  C = B log2(1+ SNR)
    Note C increases with SNR and B
  Idea of capacity is complicated
  Coding!
SNR
Capacity
B=1

## Slide 4: Example: Channel Capacity
A twisted pair telephone line has bandwidth = 4000 Hz and a SNR of 20 dB. What is the channel capacity?
SNR = 20 dB => 20 = 10 log10 (SNR)  SNR= 102 = 100
  C = B log2 (1 + SNR) = 4000 [log10(101)/log10(2)]
  = 4000[2.004/0.301] = 26,635 bps

## Slide 5: Bit Error Rate or Probability of Bit Error
Oversimplified view
  Let us say we transmit 1000 bits repeatedly 10 times
  Let us say that the receiver gets 999, 998, 1000, 995, 1000, 1000, 1000, 1000, 1000, 998 bits correctly
  The average number of bits in error for every 1000 bits sent is (1 + 2 + 0 + 5 + 0 + 0 + 0 + 0 + 0 + 2)/10 = 1 bit
  The bit error rate is 1/1000 or 10-3
Bit error rates are on the order of 10-9 in optical fiber links, higher on copper, and much higher on radio links
Depends on modulation scheme, distance, SNR, and other factors

## Slide 6: Noise and Bit Error Rate
Noise impacts BER
Higher noise => more errors
  Waterfall curve in AWGN channels
As M increases in M-ary PSK or QAM, BER increases
SNR per bit in dB
Bit Error Rate

## Slide 7: Error Control Coding
Systematically add redundant bits for error detection or correction
Part of link layer, but sometimes part of physical layer
Approaches to error control
  Error Detection + ARQ  Link layer
  Error Correction (FEC)  Physical layer
Error Control Coding
Error
Detection & ARQ
Forward Error
Correction

## Slide 8: Error control coding (2)
Error detection codes (more at link layer)
    Detect whether received word is a valid “codeword”
    May not have enough redundancy to correct bits
    Retransmit data after error
      Automatic repeat request – ARQ
Error correction codes
  Forward error correction: FEC
    Detect invalid codewords and correct into valid codeword
    Correction requires more bits than error detection
    FEC is good for one-way channels, recordings (CD-ROMs), real-time communications, deep space,...
  Generally more bits are required to protect against larger number of bit errors

## Slide 9: Multiplexing
Sending multiple signals simultaneously on the same medium
  Multiple TV channels on one coax cable, or
  Multiple radio stations on the same air space
Extremely important milestone in data communication
  Drastically reduced need for cabling
  Cabling costs are one of the biggest fixed cost components of datacomm
Slide modified from Agrawal

## Slide 10: Multiplexing
“Super-channel”:
Cable of wire pairs of fibers
CATV co-ax which is FDM-ed
Digital carrier system (T1 or SONET) which is TDM-ed
One fiber which is WDM-ed

## Slide 11: Networking without multiplexing
NYC around 1900
Slide modified from Agrawal

## Slide 12: Why multiplexing
Previous pictures show NYC before multiplexing was possible
  Multiple telephone lines between same locations required multiple physical cables
    Result: cable blanket over large metros
With multiplexing, most cables on one tower can be replaced with one cable
Slide modified from Agrawal

## Slide 13: Multiplexing categories
Send signals in different frequency bands
  Called frequency division multiplexing (FDM)
  Used with analog signals (perhaps carrying digital data)
Send signals at different times
  Called time division multiplexing (TDM)
  Used with digital signals and analog signals carrying digital data
Multiplexing in code
  Called Code Division Multiplexing (CDM)
  Used in 3G cellular systems
OFDM – Orthogonal frequency division multiplexing
  4G cellular, 802.11n and higher
Slide modified from Agrawal

## Slide 14: Frequency division multiplexing
frequency
time

## Slide 15: Frequency Division Multiplexing - Remarks
Useful bandwidth of medium exceeds required bandwidth of channel
Each signal is modulated to a different carrier frequency
Carrier frequencies separated so signals do not overlap (guard bands)
  Example: broadcast radio
Channel allocated even if no data

## Slide 16: FDM System

## Slide 17: FDM of Three Voiceband Signals

## Slide 18: Frequency Division Multiplexing Example
Using cosines and filters…

## Slide 19: Asymmetrical Digital Subscriber Line
Link between subscriber and telephone network - local loop – central office
Uses currently installed twisted pair cable
  Can carry broader spectrum of 1 MHz or more
Asymmetric
  Greater capacity downstream than upstream
Frequency division multiplexing
  Lowest 25 kHz for voice – also called Plain Old Telephone Service (POTS)
  Two bands for data (smaller for upstream)
Range 5.5km

## Slide 20: ADSL Channel Configuration
Oversimplified
Wide gap between POTS and ADSL
Asymmetric

## Slide 21: Discrete Multi-Tone (DMT)
Discrete Multi-Tone is ADSL’s modulation technique for data streams
  Called OFDM in wireless networks
Uses FDM within upstream and downstream bands
Multiple carrier signals at different frequencies
  256 downstream sub-channels at 4 kHz each (60 kbps) for a total of 15.36Mbps
  Impairments bring this down to 1.5 Mbps to 9 Mbps
  Some bits on each channel (using PSK)
  Send test signal and use sub-channels with better signal to noise ratio
Source: Stallings?

## Slide 22: Wavelength Division Multiplexing
Optical fiber has huge bandwidth of ~ 30 THz
  Several transmissions can proceed on the fiber simultaneously using different optical frequencies (wavelengths) – termed Wavelength Division Multiplexing (WDM)
  Each color (wavelength) carries separate data channel
Widely used in core backbone wired networks
  Commercial systems of 160 channels of 10 Gbps
  Fiber nonlinearities  cross channel interference short lengths
Lab systems (Alcatel) 256 channels at 39.8 Gbps each
  10 x 1 Tbps
  Over 100 km (special fiber)

## Slide 23: Types of WDM
  Basically differ in terms of channel spacing and quality of equipment
  Coarse - wider channel spacing ITU-T G.671 (cheaper)
    Most popular 4-10 channels with 20 nm spacing (10 Gbps Ethernet)
  Dense WDM > 18 wavelengths per fiber
    Abbreviated as DWDM
    Specific channels sizes standardized in an ITU Grid G.694.1
    For example, 100 GHz  0.8 nm spacing – 40 channels

## Slide 24: WDM is like FDM!

## Slide 25: WDM Operation
Same general architecture as (other) FDM
Number of sources generating laser beams at different frequencies - $$
Multiplexer consolidates sources for transmission over single fiber
  Could be a “prism” or a simple combiner
Optical amplifiers amplify all wavelengths
  Typically tens of km apart
  Mostly 1550 nm wavelength range
Demux (prism) separates channels at destination
Eventually,
Need a WDM repeater

## Slide 26: Time Division Multiplexing
  Assign a fixed time period to a transmission channel between a sender and a receiver for use of medium– termed a slot
  Different users share physical medium on slot by slot basis – take turns!
  Requires a level of synchronization among the channels and users
  Organize channel sequences into frames – a number of slots
  Note a channel is a slot in a frame – allocated even if no data is transmitted

## Slide 27: Time Division Multiplexing
time
frequency
frame
slot
Not link layerframe, but PHY layer construct

## Slide 28: TDM in Telephone Networks
  TDM is basis of digital telephone system and core network lower layer operations
  Show DS-0 to DS-1

## Slide 29: DS-1 Transmission Format
Not a packet or Ethernet frame!
1
2
3
4
5
6
7
8
Notes: The basis of the TDM hierarchy (in North America and Japan) is the DS-1 transmission
format (Figure 6.10), which multiplexes 24 channels. Each frame contains
8 bits per channel, 24 channels, plus a framing bit. Hence, each frame is 193 bits
(24 channels * 8 bits per channel + 1 framing bit = 193 bits). For voice transmission,
the following rules apply. Each channel of each frame contains one byte (8 bits) of
digitized voice data. The original analog voice signal is digitized using pulse code modulation
(PCM) at a rate of 8000 samples per second. Therefore, each channel slot and
hence each frame must repeat 8000 times per second. With a frame length of 193 bits,
we have a data rate of 8000 frames per second * 193 bits per frame = 1.544 Mbps.
For five of every six frames, 8-bit PCM samples are used. For every sixth frame,
each channel contains a 7-bit PCM byte plus a signaling bit. The signaling bits form a
stream for each voice channel that contains network control and routing information.
For example, control signals are used to establish a connection or terminate a call.
The same DS-1 format is used to provide digital data service. For compatibility
with voice, the same 1.544-Mbps data rate is used. In this case, 23 channels of
data are provided. The twenty-fourth channel position is reserved for a special sync
byte, which allows faster and more reliable reframing following a framing error.
Within each channel, 7 bits per frame are used for data, with the eighth bit used to
indicate whether the channel, for that frame, contains user data or system control
data. With 7 bits per channel, and because each frame is repeated 8000 times per
second, a data rate of 56 Kbps can be provided per channel. Lower data rates are
provided using a technique known as subrate multiplexing.
Finally, the DS-1 format can be used to carry a mixture of voice and data
channels. In this case, all 24 channels are utilized; no sync byte is provided.

## Slide 30: T1/T3 Links
Dedicated channels (private links) – private voice/data/video networks
T1
  1.536 Mbps of usable capacity on 1.544 Mbp links
  Usually in bulk or as 24 64-kbps sub-channels (DS-0s)
  Pricing often makes T1s economical when  6 DS-0s are used between two locations
  Fractional T1 - Purchase/lease ½ or ¼ of a T1
      ½ T1 = 768 kbps, ¼ T1 = 384 kbps
T3 focused on higher bandwidth users
  High capacity service (45 Mbps)
  Equivalent to 28 T1s (672 DS-0s)

## Slide 31: SONET/SDH
Synchronous Optical Network (SONET) (ANSI)
  Synchronous Digital Hierarchy (SDH) (ITU-T)
  TDM system for optical links
  Basic unit of capacity for network service providers
Signal Hierarchy
  Synchronous Transport Signal level 1 (STS-1) or Optical Carrier level 1 (OC-1)
    At 51.84 Mbps
  Carry DS-3 or group of lower rate signals
    (DS1, DS1C, DS2) plus ITU-T rates (e.g. 2.048 Mbps)
  Multiple STS-1 combined into STS-N signal
  ITU-T rates termed Synchronous Transfer Mode (STM–X)

## Slide 32: Sonet/SDH Signal Hierarchy
Notes: The SONET (Synchronous Optical Network) specification
defines a hierarchy of standardized digital data rates (Table 6.3). The lowest level,
referred to as STS-1 (Synchronous Transport Signal level 1) or OC-1 (Optical Carrier
level 1),4 is 51.84 Mbps. This rate can be used to carry a single DS-3 signal or a group
of lower-rate signals, such as DS1, DS1C, DS2, plus ITU-T rates (e.g., 2.048 Mbps).
Multiple STS-1 signals can be combined to form an STS-N signal. The signal is
created by interleaving bytes from N STS-1 signals that are mutually synchronized.
For the ITU-T Synchronous Digital Hierarchy, the lowest rate is 155.52 Mbps,
which is designated STM-1. This corresponds to SONET STS-3.
The most common data transmission speeds over SONET ranges between
155 Mbps and 2.5 Gbps. To build these data streams, SONET multiplexes lower speed
channels (with bandwidths as low as 64 Kbps) into STS frames.

## Slide 33: Mode and Multiplexing
Mode how two parties share a channel during conversation
  Simplex – one way communication (e.g., broadcast AM)
  Duplex – two way communication
    TDD: time division duplex users take turns on the channel
    FDD: Frequency division duplex – users get two channels – one for each direction of communication
    Rates need not be symmetric (ADSL)
Systems use a combination of mode and multiplexing
  Cordless phone CT2 standard: TDD/TDMA
  GSM: FDD/FDM/TDMA
    Spectrum broken up into 125 channels
    User one channel for uplink (mobile to base station) another channel for downlink (base station to mobile)
    8 users share one channel in TDM fashion

## Slide 34: GSM - TDMA/FDM/FDD
1
2
3
4
5
6
7
8
higher GSM frame structures
935-960 MHz
124 channels (200 kHz)
downlink
890-915 MHz
124 channels (200 kHz)
uplink
frequency
time
GSM TDMA frame
GSM time-slot (normal burst)
4.615 ms
546.5 µs
577 µs
tail
user data
Training
S
guard
space
S
user data
tail
guard
space
3 bits
57 bits
26 bits
57 bits
1
1
3