## Slide 1: Configuring Switch Interfaces
Liu Cui

## Slide 2: Configuring Switch Interfaces
IOS uses the term interface to refer to physical ports used to forward data to and from other devices.
Configure speed: speed {auto | 10 | 100 | 1000}
Configure duplex: duplex {auto | full | half}
The show interfaces status command lists much of the details

## Slide 3: Configure Multiple Interfaces with the interface range Command
Making the same setting on multiple consecutive interfaces: interface range FastEthernet 0/11-20

## Slide 4: Administratively Controlling Interface State with Shutdown
shutdown command to disable an interface
no shutdown command to enable an interface
show interfaces status and show interfaces
  show interfaces status: list one line of output per interface, and when shut down, lists the interface status as “disabled”.
  show interfaces: lists many lines of output per interface, giving a much more detailed picture of interface status and statistics. When shut down, the interface status comes in two parts:
    Interface is administratively down
    Line protocol is down (disabled)

## Slide 5: Removing Configuration with the no Command
With some IOS configuration commands (but not all), you can revert to the default setting by issuing a no version of the command
  If you earlier had configured speed 100 on an interface, the no speed command on that same interface reverts to the default speed setting (speed auto).
  Same idea with the duplex command: an earlier configuration of duplex half or duplex full, followed by no duplex on the same interface, reverts the configuration back to the default of duplex auto.
  If you had configured a description command with some text, to go back to the default state of having no description command at all for that interface

## Slide 6: Autonegotiation
For any 10/100 or 10/100/1000 interfaces –that is, interfaces that can run at different speeds –Cisco Catalyst switches default to a setting of duplex auto and speed auto.
As a result, those interfaces attempt to automatically determine the speed and duplex setting to use.
Alternatively, you can configure most devices, switch interfaces included, to use a specific speed and/or duplex.

## Slide 7: Autonegotiation under Working Conditions
Ethernet devices on the ends of a link must use the same standard or they cannot correctly send data. For example, a NIC cannot use 100BASE-T while the switch port on the other end of the link uses 1000BASE-T.
The IEEE autonegotiation protocol helps makes it much easier to operate a LAN when NICs and switch ports support multiple speeds. IEEE autonegotiation (IEEE 802.3u) defines a protocol that lets two UTP-based Ethernet nodes on a link negotiate so that they each choose to use the same speed and duplex settings.

## Slide 8: Autonegotiation when both nodes use the process

## Slide 9: Autonegotiation when both nodes use the process
PC1: The switch port claims it can go as fat as 1000 Mbps, but PC1’s NIC claims a top speed of 10 Mbps. Both the PC and switch choose the best speed both support (10 Mbps) and the best duplex (full).
PC2: PC2 claims a best speed of 100 Mbps, which means it can use 10BASE-T or 100BASE-T. The switch port and NIC negotiate to use the best speed of 100 Mbps and full duplex.
PC3: It uses a 10/100/1000 NIC, supporting all three speeds and standards, so both the NIC and switch port choose 1000 Mbps and full duplex.

## Slide 10: Autonegotiation when only one uses the process
IEEE autonegotation defines some rules (defaults) that nodes should use as defaults when autonegotiation fails –that is, when a node tries to use autonegotiation but hears nothing from the device. The rules:
  Speed: Use your slowest supported speed
  Duplex: if your speed = 10 or 100, use half duplex; otherwise, use full duplex.
Cisco switches can make a better choice than that base IEEE logic, because Cisco switches can actually sense the speed used by other nodes, even without IEEE autonegotiation. As a result, Cisco switches use this slightly different logic to choose the speed when autonegotiation fails:
  Speed: Sense the speed, but if that fails, use the IEEE default
  Duplex: Use the IEEE defaults

## Slide 11: Autonegotiation when only one uses the process

## Slide 12: Autonegotiation when only one uses the process
PC1: The switch receives no autonegotation messages, so it senses the electrical signal to learn that PC1 is sending data at 100 Mbps. The switch uses the IEEE default duplex based on the 100 Mbps speed (half duplex).
PC2: The switch uses the same steps and logic as with the link to PC1, except that the switch chooses to use full duplex because the speed is 1000 Mbps.
PC3: The user picks poorly, choosing the slower speed (10 Mbps) and the worse duplex setting (half). However, the Cisco switch senses the speed without using IEEE autonegotation and then uses the IEEE duplex default for 10-Mbps links (half duplex).

## Slide 13: Autonegotation and LAN Hubs
LAN hubs also impact how autonegotation works.
Basically, hubs do not react to autonegotiation messages, and they do not forward the messages.
As a result, devices connected to a hub must use the IEEE rules for choosing default settings, which often results in the devices using 10 Mbps and half duplex.

## Slide 14: Port Security
If the network engineer knows what devices should be cabled and connected to particular interfaces on a switch, the engineer can use port security to restrict that interface so that only the expected devices can use it.
This reduces exposure to attacks in which the attacker connects a laptop to some unused switch port.
When that inappropriate device attempts to send frames to the switch interface, the switch can take different actions, ranging from simply issuing informational messages to effectively shutting down the interface.

## Slide 15: Concept behind Port Security
Define a maximum number of source MAC addresses allowed for all frames coming in the interface.
Watch all incoming frames, and keep a list of all source MAC addresses, plus a counter of he number of different source MAC addresses.
When adding a new source MAC address to the list, if the number of MAC addresses pushes past the configured maximum, a port security violation has occurred. The switch takes action (the default action is to shut down the interface).

## Slide 16: Configuring Port Security
Step 1: Make the switch interface either a static access or trunk interface using the switchport mode access or the switchport mode trunk interface subcommands, respectively.
Step 2: Enable port security using the switchport port-security interface subcommand.
Step 3: (Optional) Override the default maximum number of allowed MAC addresses associated with the interface (1) by using the switchport port-security maximum number interface subcommand.
Step 4: (Optional) Override the default action to take upon a security violation (shutdown) using the switchport port-security violation {protect | restrict | shutdown} interface subcommand.
Step 5: (Optional) Predefine any allowed source MAC addresses for this interface using the switchport port-security mac-address mac-address command. Use the command multiple times to define more than one MAC address.
Step 6: (Optional) Tell the switch to “sticky learn” dynamically learned MAC addresses with the switchport port-security mac-address sticky interface subcommand.

## Slide 17: Verifying Port Security
show port-security interface {fastEhternet 0/1} lists the configuration settings for port security on an interface, plus it lists several important facts about the current operation of port security, including information about any security violations.

## Slide 18: Port Security Violation Actions
The switch can be configured to use one of three actions when a violation occurs.
All three options cause the switch to discard the offending frame, but some of the options make the switch take additional actions.
The actions include the sending of syslog messages to the console, sending SNMP trap messages to the network management station, and disabling the interface.

## Slide 19: Port Security MAC Addresses as Static and Secure but Not Dynamic
Once a switch port has been configured with port security, the switch no longer considers MAC addresses associated with that port as bing dynamic entries as listed with the show mac address-table dynamic EXEC command.
Even if the MAC addresses are dynamically learned, once port security has been enabled, you need to use one of these options to see the MAC table entries associated with ports using port security:
  Show mac address-table secure: Lists MAC addresses associated with ports that use port security
  Show mac address-table static: Lists MAC addresses associated with ports that use port security, as well as any other statically defined MAC addresses

## Slide 20: Lab Assignment
Under Configuration Scenarios, please click Switching.
You need to do all labs (2):
  Switch Interfaces and Forwarding
  Switch Security