## Slide 1: Lecture 7a
The Link Layer

## Slide 2: Simplified Web Browsing
Message from Alice’s Browser
Web server process gets message
TCP Segments Created
TCP segment is recovered, assembled
IP datagrams carry TCP segments
IP datagram is picked up from frame
Ethernet in Alice’s PC creates frame
Ethernet in server gets frame, checks for errors
Ethernet cable carries signal to edge router
Cable carries the signal representing Ethernet frame to server machine
Ethernet in router gets frame , checked for errors
Puts it in Ethernet frame
Transport
There is a one-to-one correspondence
between layers in the two end points
There is a structured “flow”
between layers at each end
Looks at IP DA for routing
Edge router receives IP datagram

## Slide 3: Simplified Internet Structure
Hierarchical
Access network has a router that connects it to a regional ISP
Regional ISPs connect to global ISPs
Remember: Router = packet switch
Transport
mobile network
global ISP
regional ISP
home
network
institutional
network
Figure from Kurose-Ross
Notes: Most enterprise computer networks can be separated into two general types of technology: local area networks (LAN) and wide-area networks (WAN). LANs typically connect nearby devices: devices in the same room, in the same building, or in a campus of buildings. In contrast, WANs connect devices that are typically relatively far apart. Together, LANs and WANs create a complete enterprise computer network, working together to do the job of a computer network: delivering data from one device to another.
Many types of LANs have existed over the years, but today’s networks use two general types of LANs: Ethernet LANs and wireless LANs. Ethernet LANs happen to use cables for the links between nodes, and because many types of cables use copper wires, Ethernet LANs are often called wired LANs. In comparison, wireless LANs do not use wires or cables, instead using radio waves for the links between nodes.

## Slide 4: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
Slide modified from Kurose-Ross
Uses “link or MAC address” at frame level
Alice
Bob
Uses “IP address” at datagram/network level
Signal

## Slide 5: Remarks
Observe carefully
  How much of the physical layer bits are “moved” up the stack at various nodes
What does a “layer-2” switch do?
What does a router do?
  Does it look at the IP datagram? At the TCP segment? At the application payload?
When is a TCP segment reassembled?
  This is end-to-end

## Slide 6: Link Layer
Hosts and routers are nodes
Communication channels that connect adjacent nodes along communication path are links
  wired links, wireless links
Layer-2 packet is a frame, encapsulates IP datagram
Note, datagram maybe transferred by different link layer protocols over different links
“link”
data-link layer has responsibility of transferring data from one node
to adjacent node over a link

## Slide 7: Typical SOHO LANs
Notes: Figure shows a drawing of a SOHO Ethernet LAN. The figure shows a single LAN switch, five cables, and five other Ethernet nodes: three PCs, a printer, and one network device called a router. The router connects the LAN to the WAN, in this case to the Internet.
Although figure shows a simple Ethernet LAN, many SOHO Ethernet LANs today combine the router and switch into a single device. Vendors sell consumer-grade integrated networking devices that work as a router and Ethernet switch, as well as doing other functions. These devices typically have “router” on the packaging, but many models also have four-port or eight-port Ethernet LAN switch ports built in to the device.
Typical SOHO LANs today also support wireless LAN connections. Ethernet defines wired LAN technology only; in other words, Ethernet LANs use cables. However, you can build one LAN that uses both Ethernet LAN technology as well as wireless LAN technology, which is also defined by IEEE. Wireless LANs, defined by the IEEE using standards that begin with 802.11, use radio waves to send the bits from one node to the next.
Most wireless LANs rely on yet another networking device: a wireless LAN access point (AP). The AP acts somewhat like an Ethernet switch, in that all the wireless LAN nodes communicate with the Ethernet switch by sending and receiving data with the wireless AP. Of course, as a wireless device, the AP does not need Ethernet ports for cables, other than for a single Ethernet link to connect the AP to the Ethernet LAN.

## Slide 8: Typical Enterprise LANs
Notes: Enterprise networks have similar needs compared to a SOHO network, but on a much larger scale. For example, enterprise Ethernet LANs begin with LAN switches installed in a wiring closet behind a locked door on each floor of a building. The electricians install the Ethernet cabling from that wiring closet to cubicles and conference rooms where devices might need to connect to the LAN. At the same time, most enterprises also support wireless LANs in the same space, to allow people to roam around and still work and to support a growing number of devices that do not have an Ethernet LAN interface.
Figure shows a conceptual view of a typical enterprise LAN in a three-story building. Each floor has an Ethernet LAN switch and a wireless LAN AP. To allow communication between follors, each per-floor switch connects to one centralized distribution switch. For example, PC3 can send data to PC2, but it would first flow through switch SW3 to the first floor to the distribution switch (SWD) and then back up through switch SW2 on the second floor.
The figure also shows the typical way to connect a LAN to a WAN using a router. LAN switches and wireless access points work to create the LAN itself. Routers connect to both the LAN and the WAN. To connect to the LAN, the router simply uses an Ethernet LAN interface and an Ethernet cable.

## Slide 9: Functions of the Data-Link layer
ATIS Telecom glossary 2007
  Transfer data between devices on the same network
  Detect and possibly correct errors that may occur in the Physical Layer
Ethernet is the most common end-user implementation of the data-link layer
  Most corporate desktops
WiFi is the most common wireless link layer
  Cellular data (3G/4G) increasingly common
Slide modified from Agrawal

## Slide 10: Types of links
Point-to-point
  Bluetooth for cable replacement (shared medium)
  Point-to-point link between switch and server
Broadcast (shared wire or medium) link
  Ethernet, WiFi
  Upstream Cable modem
http://www.bitmedia.com/ar96/images/pdc2000pb.jpg

## Slide 11: Link Layer Services
Framing
  Encapsulate datagram into frame, adding header, trailer, addressing
  Format/encode for physical layer
Channel access (if shared medium) (MAC)
  Control who uses channel and routing/reception of data
Communication Mode
  Simplex – one way communication (e.g., broadcast AM)
  Duplex – two way communication
    TDD (half Duplex) vs. Full Duplex
Flow Control:
  Pacing between adjacent sending and receiving nodes
Reliable delivery between adjacent nodes
  Error Detection
    receiver detects presence of errors: asks sender for retransmission or drops frame (ARQ)
  Error Correction
    receiver identifies and corrects bit error(s) without resorting to retransmission (FEC)
Also at the transport layer – “end-to-end”

## Slide 12: Adaptors Communicating
link layer implemented in “adaptor” (aka NIC)
  Ethernet card, UMTS/LTE, 802.11 card
sending side:
  encapsulates datagram in a frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, does flow control, etc.
  extracts data, passes to rcving node
adapter is semi-autonomous
link & physical layers
sending
node
frame
receiving
node
data
frame
adapter
adapter
link layer protocol

## Slide 13: Link Layer Services – This Lecture
Framing and Addressing
Channel Access (or Medium Access Control)
Next lecture
  Error control coding

## Slide 14: Link Layer Framing
NPDU = Network Packet Data Unit
How does Router know the “frame” is meant for it?

## Slide 15: Addressing in the “Header”
Data Link Layer addresses
  Locally significant address used to identify node
  Often called Medium Access Control (MAC) address
    48 bits in Ethernet, WiFi
  Can be burned (hardware) into NIC
Hosts are known to a subnet (e.g., LAN) by their local attachment MAC address
  An IP address does not help deliver a packet on a link
NIC = Network Interface Card

## Slide 16: Example: Framing in Ethernet
Link Layer framing generally involves
  Header and Tail Blocks to encapsulate Network Layer packet
  Header and Tail blocks normally include Link Layer address and error control bits
  Format depends on specific Layer 2 protocol
General packet format in Ethernet
IP Datagram is here
What is CRC?
These are the MAC addresses
# of bits

## Slide 17: Example: Framing in WiFi
Number of addresses
Duration field – later
Fragmentation (in Seq. Control)
What is CRC?
IP Datagram is here
These are the MAC addresses

## Slide 18: Channel Access: Medium Access Control or MAC
MAC protocols needed when using a single shared broadcast link
Two or more simultaneous transmissions by nodes can result in “interference”
  Collision if node receives two or more signals at the same time
To Internet

## Slide 19: MAC Protocols: a taxonomy
Channel Partitioning
  Divide channel into smaller “pieces” (time slots, frequency)
  Allocate piece to node for exclusive use
  Examples are TDM and FDM
Random Access
  Channel not divided, allow collisions
  “Recover” from collisions
“Taking turns”
  Nodes take turns, but nodes with more to send can take longer turns
Image Source: http://www.carinsurancecomparison.com/Images/collision-coverage.jpg

## Slide 20: Pros and Cons
Channel partitioning MAC protocols:
  Share channel efficiently and fairly at high load
  Inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
Random access MAC protocols
  Efficient at low load: single node can fully utilize channel
  High load: collision overhead
“Taking turns” protocols
  Look for best of both worlds!

## Slide 21: Channel Partitioning MAC protocols: TDMA
TDMA: time division multiple access
  Access to channel in "rounds"
  Each station gets fixed length slot (e.g., length = maximum packet transmission time) in each round
  Unused slots go idle
Example: 6-station LAN, 1,3,4 have packet, slots 2,5,6 idle
  TDM (Time Division Multiplexing): channel divided into N time slots, one per user; inefficient with low duty cycle users and at light load.
  FDM (Frequency Division Multiplexing): frequency subdivided.
Two types of frames, be careful

## Slide 22: Random Access Protocols
When node has packet to send
  Transmit at full channel data rate R.
  No a priori coordination among nodes
Two or more transmitting nodes ➜ “collision”
Random access MAC protocol specifies:
  How to detect collisions
  How to recover from collisions (e.g., via delayed retransmissions)
Examples of random access MAC protocols:
  ALOHA, slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 23: ALOHA
1970: ALOHAnet satellite network in Hawaii
Transmit a link level frame whenever you want!
  Wait for an acknowledgement
If there is a collision, wait till a random amount of time and retransmit
  Collision => entire packet transmission time wasted for everyone
collision
This is a link layer “Frame”

## Slide 24: Slotted ALOHA
Fix the starting/ending times to specific values (slots)
  Say t, t+F, t+2F and so on
  This reduces the number of collisions
Under heavy traffic conditions, the best success rate is only 36%
  Under light traffic loads, it does not matter
Where is this used?
  All cellular networks with some modifications

## Slide 25: Can we do better?
Carrier sense multiple access (CSMA)
  “Sense” the medium to see if it is occupied before transmitting
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission

## Slide 26: Collisions in CSMA
spatial layout of nodes
collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
note: role of distance & propagation delay in determining collision probability

## Slide 27: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing channel wastage
Collision detection:
  Easy in wired LANs: measure signal strengths, compare transmitted, received signals
  Difficult in wireless LANs: may be out of range of other user transmitting to same Access Point

## Slide 28: Taking Turns MAC protocols
Token passing (old token ring and bus networks)
Control token passed from one node to next sequentially.
Token message
Concerns:
  Token overhead
  Latency
  Single point of failure (token)

## Slide 29: Polling and Scheduling
Bluetooth uses polling
Scheduling is used on cellular links
  It is sometimes called “reservation”
(Master)
Figure Source: Forouzan