## Slide 1: Lecture 8a
Link Layer 2: Error Control Coding

## Slide 2: Error detection
As the packet moves from source to destination, it can get errors
  Just as cars can get flat tires from driving
Errors are caused due to the imperfections of the physical world
  Noise from power spikes, outages etc.
These errors have to be detected
  And (perhaps) corrected
Slide modified from Agrawal

## Slide 3: Error correction in human communication
Some human error-correction techniques
  Receiver reads back on telephone
    Credit card number, phone number etc.
      Not reliable in computer networks because of possible error-cancellation
  Redundant data
    Don’t just say tomorrow
      Say tomorrow, Thursday, Nov. 16, 2000
  Sender contact information
    For clarification if necessary
Slide modified from Agrawal

## Slide 4: Error correction in computer communication
The general approach to error detection in human communications is not effective in computer communications because of possible error cancellations
Slide modified from Agrawal

## Slide 5: Error correction in computer communication
The general approach to error detection in data communications is to add some meta-data to the original data
  The meta-data is generated from the data itself
  The receiver can re-compute the meta-data and compare the result with the meta-data sent by the sender
Accept if results match, reject otherwise
Slide modified from Agrawal

## Slide 6: Error correction – simple example
Say we want to send HELLO
  We could code it (in decimal) as 8 5 12 12 15 (location in the alphabet)
  A simple meta-data would be to add all the digits till you get a single digit
  8 + 5 + 12 + 12 + 15 = 52
  5 + 2 = 7
  Send 8 5 12 12 15 7
Slide modified from Agrawal

## Slide 7: Error correction problems
If everything goes well, the receiver will get
  8 5 12 12 15 7
    It knows that the 7 is the “meta-data”
    It calculates 8 + 5 + 12 + 12 + 15 = 52
    5 + 2 = 7
    Hence, data was received without error
But this scheme is too naïve
  What if we receive 8 5 11 13 15 7
  Or 2 2 11 13 15 7
Slide modified from Agrawal

## Slide 8: Classification of Error Control Coding
Error Control Coding
Waveform
Coding
Block
Coding
Convolutional
Coding
Turbo
Coding
Error Control Coding
Error
Detection & ARQ
Forward Error
Correction
Trellis
Coded
Modulation

## Slide 9: Block Codes
(n,k) block codes
  k = number of data bits in block
    Data word length
  n-k = number of parity check bits added
  n = length of codeword or code block
  (n-k)/n = overhead or redundancy
    Lower is more efficient
  k/n = code rate Rc
    Higher is more efficient, but less powerful
Block
Encoder
k bit data block
n bit codeword
n – k parity check bits
k data bits
Simple Block code

## Slide 10: Design of Error Correcting/Detecting Codes
There is a lot of theory involved
  Groups, rings and fields
  Algebra!
We will look at some simple schemes
Example:
  Single bit even parity (4,3) code
  23 valid codewords
  24 total 4-bit words
What is the Code Rate?
Message Word | Codeword
0 0 0 | 0 0 0 0
0 0 1 | 0 0 1 1
0 1 0 | 0 1 0 1
0 1 1 | 0 1 1 0
1 0 0 | 1 0 0 1
1 0 1 | 1 0 1 0
1 1 0 | 1 1 0 0
1 1 1 | 1 1 1 1
Even parity check – what is n? what is k?

## Slide 11: Cyclic Codes
Cyclic or polynomial codes: a subclass of block codes
  Cyclic shifts of valid codeword is another valid codeword
    If C=(cn-1,..., c0) is codeword then so is (cn-2,..., c0, cn-1)
  Sum of two codewords (modulo 2) is also a codeword
Advantage of easy encoder/decoder implementation resulting from this structure
Most block codes in practice today are cyclic or related

## Slide 12: Properties of cyclic codes
Each codeword can be represented as a polynomial
  [cn-1 cn-2 cn-3 … c0] = c0 x0 + c1 x1 + … + cn-1 xn-1 = c(x)
  Example: 1010001 = 1 + x4 + x6
  What is the degree of c(x)?
A generator polynomial is used for creating the codeword and detecting errors
  Generator polynomial is g(x) of degree n - k

## Slide 13: Creating and Decoding Cyclic Codes
Given the generator polynomial g(x)
  Multiply the “message polynomial” u(x) by xn-k
  Divide xn-k u(x) by g(x)  the remainder is b(x)
  Add b(x) to xn-k u(x) to get the code polynomial c(x)
Let the received polynomial be r(x)
  Divide r(x) by g(x)
  The remainder s(x) is the “syndrome” polynomial
    What can you say about the degree of s(x)?
    If s(x) = 0, it is assumed there are NO errors

## Slide 14: Modulo-2 division rules
Modulo-2 division uses Exclusive OR for subtraction operations during division
0 – 0 = 0
0 – 1 = 1
1 – 0 = 1
1 – 1 = 0
Slide modified from Agrawal
Adding and Subtracting are the same!

## Slide 15: Example (Hamming Code)
The generator polynomial is
  g(x) = 1 + x + x3
Encode the message sequence u = [1000]
Compute the syndrome for r = [100 1000]

## Slide 16: Cyclic redundancy check (CRC)
Most commercial data communication technologies use CRC
CRC-32 is used in Ethernet
  99.99999998% reliable for errors greater than 32 bits long
The generator polynomial is
g(x) = 1+ x + x2 + x4 + x5 + x7 + x8 + x10 + x11 + x12 + x16 + x22 + x23 + x26 + x32
Slide modified from Agrawal
See also: http://www.xilinx.com/support/documentation/application_notes/xapp209.pdf

## Slide 17: CRC-32 capabilities
CRC-32 can detect all errors affecting less than 33 (n + 1) bits
CRC can detect all errors affecting odd number of bits
CRC-32 can reasonably reliably detect errors affecting more than 33 (n + 1) bits
Slide modified from Agrawal