## Slide 1: Configuring Basic Switch Management
Liu Cui

## Slide 2: Securing the Switch CLI
By default, a Cisco Catalyst switch allows anyone to connect to the console port, access user mode, and then move on to enable and configuration modes without any kind of security.
That default makes sense, give that if you can get to the console port of the switch, you already have control over the switch physically.
However, everyone needs to operate switches remotely, and the first step in that process is to secure the switch so that only the appropriate users can access the switch command-line interface (CLI)

## Slide 3: Securing the Switch CLI
Protecting access to enable mode: an attacker could reload the switch or change the configuration.
Protecting user mode: attackers can see the status of the switch, learn about the network, and find new ways to attack the network
All remote access and management protocols require that the switch IP configuration be completed and working. A switch’s IPv4 configuration has nothing to do with how a Lyaer 2 switch forwards Ethernet frames, but to Telnet and Secure Shell (SSH) to a switch, the switch needs to be configured with an IP address.

## Slide 4: Scope of this Chapter
Securing user mode and privileged mode with simple passwords
Securing user mode access with local usernames
Securing user mode access with external authentication servers
Securing remote access with Secure Shell (SSH)

## Slide 5: Securing User Mode and Privileged Mode with Simple Passwords
Secure access to user mode: uses a password only, with no username, with one password for console users and a different password for Telnet users (also called vty password, because the configuration sits in vty line configuration model).
Secure enable mode: once in user mode, the user types the enable command. This command prompts the user for this enable password; if the user types the correct password, IOS moves the user to enable mode.

## Slide 7: Configuration checklist
Step 1: Configure the enable password with the enable secret password-value command
Step 2: Configure the console password:
  Use the line con 0 command to enter console configuration mode.
  Use the login subcommand to enable console password security using a simple password.
  Use the password password-value subcommand to set the value of the console password.

## Slide 8: Configuration checklist
Step 3: Configure the Telnet (vty) password:
  Use the line vty 0 15 command to enter vty configuration model for all 16 vty lines (numbered 0 though 15)
  Use the login subcommand to enable password security for vty sessions using a simple password.
  Use the password password-value subcommand to set the value of the vty password.

## Slide 9: Securing User Mode Access with Usernames and Passwords
Two ways:
  Local: configured directly on the switch
    Set up username and password
    Set login local for console and vty (telnet)
  External authentication servers
    Using a username/password configured directly on the switch causes some administrative headaches. For instance, every switch and router needs the configuration for all users who might need to log in to the devices.
    Cisco switches allow an external server called an authentication, authorization, and accounting (AAA) server, which holds the usernames/passwords.
    The switch or router simply sends a message to the AAA server asking whether the username and password are allowed, and the AAA server replies.

## Slide 10: Securing User Mode Access with Local Usernames and Passwords
Step 1: Use the username name secret password global configuration command to add one or more username/password pairs on the local switch
Step 2: Configure the console to use locally configured username/password pairs:
  Use the line con 0 command to enter console configuration mode.
  Use the login local subcommand to enable the console to prompt for both username and password, checked versus the list of local usernames/passwords.
  (Optional) Use the no password subcommand to remove any existing simple shared passwords, just for good housekeeping of the configuration file.

## Slide 11: Securing User Mode Access with Local Usernames and Passwords
Step 3: Configure Telnet (vty) to use locally configured username/password pairs.
  Use the line vty 0 15 command to enter vty configuration model for all 16 vty lines.
  Use the login local subcommand to enable the switch to prompt for both username and password for all inbound Telnet users, checked versus the list of local usernames/passwords.
  (Optional) User the no password subcommand to remove any existing simple shared passwords, just for good housekeeping of the configuration file.

## Slide 12: Securing Remote Access with Secure Shell
Telnet has one serious disadvantage: all data in the Telnet session follows as clear text, including the password exchanges. So, anyone that can capture the messages between the user and the switch can see the passwords.
SSH encrypts all data transmitted between the SSH client and server, protecting the data and passwords.
SSH can user the same local login authentication method as Telnet, with the locally configured username and password.
SSH cannot rely on a password only.

## Slide 13: Securing Remote Access with Secure Shell
IOS uses the three SSH-specific configuration commands to create the SSH encryption keys. The SSH server uses the fully qualified domain name (FQDN) of the switch as input to create that key. The term FQDN combines the hostname of a host and its domain name. Then the third command, the crypto key generate rsa command, generates the SSH encryption keys
Example:
    hostname sw1
    ip domain-name example.com
    crypto key generate rsa

## Slide 14: Securing Remote Access with Secure Shell
By default, switches support both SSH and Telnet on the vty lines. However, because Telnet is a security risk, you could disable Telnet to enforce a tighter security policy, use the transport input {all | none | telnet | ssh} vty subcommand in vty mode:
  transport input all or transport input telnet ssh: support both Telnet and SSH
  transport input none: support neither
  transport input telnet: support only Telnet
  transport input ssh: support only SSH

## Slide 15: Enabling IPv4 for Remote Access
To allow Telnet or SSH access to the switch, and to allow other IP-based management protocols (for example, Simple Network Management Protocol) to function as intended, the switch needs an IP address, as well as a few other related settings.
The IP address has nothing to do with how switches forward Ethernet frames; it simply exists to support overhead management traffic.

## Slide 16: Enabling IPv4 for Remote Access
The switch uses a network interface card (NIC)-like concept called a switched virtual interface (SVI), or more commonly, a VLAN interface, that acts like the switch’s own NIC.
Then the settings on the switch look something like a host, with the switch configuration assigning IP settings, like an IP address, to this VLAN interface.

## Slide 17: Enabling IPv4 for Remote Access
By using interface vlan1 for the IP configuration, the switch can then send and receive frames on any of the ports in VLAN1. In a Cisco switch, by default, all ports are assigned to VLAN1. The network manager can create many VLANs.

## Slide 18: Configuring IPv4 on a Switch
Step 1: use the interface vlan 1 command in global configuration mode to enter interface VLAN1 configuration mode.
Step 2: use the ip address ip-address mask command in interface configuration model to assign an IP address and mask
Step 3: use the no shutdown command in interface configuration mode to enable the VLAN1 interface if it is not already enabled
Step 4: add the ip default-gateway ip-address command in global configuration mode to configure the default gateway.
Step 5 (optional): add the ip name-server ip-address1 ip-address2 … command in global configuration mode to configure the switch to use Domain Name Systems (DNS) to resolve names into their matching IP address.

## Slide 19: Configuring a Switch to Learn Its IP Address with DHCP
The switch can also use Dynamic Host Configuration Protocol (DHCP) to dynamically learn its IPv4 settings. Basically, all you have to do is tell the switch to use DHCP on the interface, and enable the interface.
Step 1: Enter VALN1 configuration model using the interface vlan 1 global configuration command, and enable the interface using the no shutdown command as necessary.
Step 2: Assign an IP address and mask using the ip address dhcp interface subcommand.

## Slide 20: Verifying IPv4 on a Switch
The switch IPv4 configuration can be checked in several places.
  show running-config command: current configuration
  show interfaces vlan 1 command: IP address and mask information
  show dhcp lease command: leasesed IP address and other parameters