## Slide 1: Configuring IPv4 Addresses and Static Routes
Liu Cui

## Slide 2: IP Routing
IP routing –the process of forwarding IP packets –delivers packets across entire TCP/IP networks, from the device that originally builds the IP packet to the device that is supposed to receive the packet.
In other words, IP routing delivers IP packets from the sending host to the destination host.

## Slide 3: The Routing Process of the Host
Step 1. If the destination is local, send directly:
  A. Find the destination host’s MAC address. Use the already-known Address Resolution Protocol (ARP) table entry, or use ARP messages to learn the information.
  B. Encapsulate the IP packets in a data-link frame, with the destination data-link address of the destination host.
Step 2. If the destination is not local, send to the default gateway:
  A. Find the default gateway’s MAC address. Use the already-known APR table entry, or user ARP messages to learn the information.
  B. Encapsulate the IP packets in a data-link frame, with the destination data-link address of the default gateway.

## Slide 4: The Routing Process of the Router
Step 1. For each received data-link frame. Process it if
  A. The frame has no errors (per the data-link trailer Frame Check Sequence field)
  B. The frame’s destination data-link address is the router’s address (or an appropriate multicast or broadcast address).
Step 2. If choosing the process the frame at Step 1, de-encapsulate the packet from inside the data-link frame.
Step 3. Make a routing decision. To do so, compare the packet’s destination IP address to the routing table and find the route that matches the destination address. This route identifies the outgoing interface of the router and possibly the next-hop router.
Step 4. Encapsulate the packet into a data-link frame appropriate for the outgoing interface. When forwarding out LAN interfaces, use ARP as needed to find the next device’s MAC address.
Step 5. Transmit the frame out the outgoing interface, as listed in the matched IP route.

## Slide 5: Configuring IP addresses and Connected Routes
Cisco routers enable IPv4 routing globally, by default.
Then, to make the router be ready to route packets on a particular interface, the interface must be configured with an IP address and the interface must be configured such that it comes up, reaching a “line status up, line protocol up” state.
Only at that point can routers route IP packets in an out a particular interface.

## Slide 6: Configuring IP addresses and Connected Routes
After a router can route IP packets out one or more interfaces, the router needs some routes. Routers can add routes to their routing tables through three methods:
  Connected routes: Added because of the configuration of the ip address interface subcommand on the local router (chapter 18)
  Static routes: Added because of the configuration of the ip route global command on the local router (chapter 18)
  Routing protocols: Added as a function by configuration on all routers, resulting in a process by which routers dynamically tell each other about the network so that they all learn routes (chapter 19)

## Slide 7: Connected Routes
ip address command
  A Cisco router automatically adds a route to its routing table for the subnet connected to each interface, assuming that the following two facts are true:
    The interface is in a working state. In other words, the interface status in the show interfaces command lists a line status of up and a protocol status of up.
    The interface has an IP address assigned through the ip address interface subcommand.
  The router does the math, taking the interface IP address and mask, and calculating the subnet ID.
  However, the router only needs that route when the interface is up and working, so the router includes a connected routed in the routing table only when the interface is working.

## Slide 8: Connected Routes
The ARP Table on a Cisco Router
  After a router has added these connected routes, the router can route IPv4 packets between those subnets. To do so, the router makes use of its IP ARP table.
  The IPv4 ARP table lists the IPv4 address and matching MAC address of hosts connected to the same subnet as the router.
    When forwarding a packet to a host on the same subnet, the router encapsulates the packet, with a destination MAC address as found in the ARP table.
    If the router wants to forward a packet to an IP address on the same subnet as the router, but does not find an ARP table entry for that IP address, the router will use ARP messages to learn that device’s MAC address.

## Slide 9: Connected Routes
Routing Between Subnets on VLANs
  Three options exist for connecting a router to each subnet on a VLAN.
    Use a router, with one router LAN interface and cable connected to the switch for each and every VLAN (Typically not used).
    Use a router, with a VLAN trunk connecting to a LAN switch.
    Use a Layer 3 switch

## Slide 10: Connected Routes
Configuring Routing to VLANs Using 802.1Q on Routers
Also called router-on-a-stick (ROAS)
ROAS uses router VLAN trunking configuration to give the router a logical router interface connected to each VLAN, and therefore each subnet that sits on a separate VLAN.
That trunking configuration revolves around subinterfaces. The router needs to have an IP address/mask associated with each VLAN on the trunk. However, the router uses only one physical interface on which to configure the ip address command.
Cisco solves this problem by creating multiple virtual router interfaces, one associated with each VLAN on that trunk. Cisco calls these virtual interfaces subinterfaces.

## Slide 11: Connected Routes
Steps to configure 802.1Q trunking on a router
  Step 1. Use the interface type number.subint command in global configuration model to create a unique subinterface for each VLAN that needs to be routed.
  Step 2. Use the encapsulation dot1q vlan_id command in subinterface configuration mode to enable 802.1Q and associate one specific VLAN with the subinterface.
  Step 3. Use the ip address address mask command in subinterface configuration mode to configure IP settings.

## Slide 12: Connected Routes
Configuring Routing to VLANs Using a Layer 3 Switch
  A Layer 3 switch is one device that does two primary functions: Layer 2 LAN switching and Layer 3 IP routing.
  The layer 2 switch function forwards frames inside each VLAN, but it will not forward frames between VLANs.
  The Layer 3 forwarding logic –routing –forwards IP packets between VLANs.

## Slide 13: Connected Routes
How to configure Layer 3 switching
  Step 1. On some older models of switches, enable hardware support for IPv4 routing. For example, in 2960 switches, use the sdm prefer lanbase-routing in global configuration model and reload the switch.
  Step 2. Use the ip routing command in global configuration mode to enable IPv4 routing on the switch.
  Step 3. Use the interface vlan valn_id command in global configuration mode to create VLAN interfaces for each vLAN for which the Layer 3 switch is routing packets.
  Step 4. Use the ip address address mask command in interface configuratio mode to configure an IP address and mask on the VLAN interface, enabling IPv4 on that VLAN interface.
  Step 5. Use the no shutdown command in interface configuration mode to enable the VLAN interface.

## Slide 14: Static Route
Networks use static routes –routes added to a routing table through direct configuration –much less often than dynamic routing.
Static Route Configuration
  IOS allows the definition of individual static routes using the ip route global configuration command.
  Every ip route command defines a destination that can be matched, usually with a subnet ID and mask. The command also lists the forwarding instructions, typically listing either the outgoing interface or the next-hop router’s IP address.
  IOS then takes that information and adds that route to the IP routing table.

## Slide 15: Static Route
Static Route Configuration (cont)
  Example code:
    ip route 172.16.2.0 255.255.255.0 172.16.4.2
    ip route 172.16.3.0 255.255.255.0 s0/0/1
  Two example ip route commands show the two different styles.
    The first command shows subnet 172.16.2.0 mask 255.255.255.0 can be reached through router that has the ip address: 172.16.4.2.
    The second route has the same kind of logic, but instead of identifying the next router by IP address, it lists the local router’s outgoing interface.
  Check: use show ip route static command to check the route information.

## Slide 16: Static Route
Static Host Routes
  A host route is a route for a single host address, as noted with the IP address and a /32 mask.
  The ip route command can create static routes for remote hosts by using a mask of 255.255.255.255
  Example code:
    ip route 10.1.1.0 255.255.255.0 10.2.2.2
    ip route 10.1.1.9 255.255.255.255 10.9.9.9
  Note that these two routes overlap: a packet sent to 10.1.1.9 that arrives at the router would match both routes. When that happens, routers use the most specific route (that is, the route with the longest prefix length). So, a packet sent to 10.1.1.9 would be forward to next-hop router 10.9.9.9.

## Slide 17: Static Route
Static Routes with No Competing Routes
  Competing routes: different routes that reach the same subnet.
  The other routes could be learned by a routing protocol, or be another static route.
  If the configured route has no competing routes, the router still checks a few rules before adding the route to its IP routing table:
    For ip route commands that list an outgoing interface, that interface must be in an up/up state.
    For ip route commands that list a next-hop IP address, the local router must have a route to reach that next-hop address.

## Slide 18: Static Route
Static Routes with Competing Routes
  Next, consider the case in which a static route competes with other static routes or routes learned by a routing protocol. That is, the ip route command defines a route to a subnet, but the router also knows of other static or dynamically learned routes to reach that same subnet.
  In these cases, the router must first decide which routing source has the better administrative distance, with lower being better, and then use the route learned from the better source.
  IOS considers static routes better than OSPF-learned routes. By defulat, IOS gives static route an administrative distance of 1 and OSPF routes an administrative distance of 110.

## Slide 19: Static Route
Static Routes with Competing Routes (Cont)
  To instead prefer the OSPF routes, the configuration would need to change the administrative distance settings and use a floating static route.
  A floating static route floats or moves into and out of the IP routing table depending on whether the better (lower) administrative distance route learned by the routing protocol happens to exist currently.
  Basically, the router ignores the static route during times when the better routing protocol route is known.
  To implement a floating static route, just override the default administrative distance on the static route, making the value larger than the default administrative distance of the routing protocol.
    For example: ip route 172.16.2.0 255.255.255.0 172.16.5.3 130
    It sets the static route’s administrative distance to 130.
  Finally, use show ip route command to list all status

## Slide 20: Static Route
Static Default Routes
  When a router tries to route a packet, the router might not match the packet’s destination IP address with any route. When that happens, the router normally just discards the packet.
  Routers can be configured so that they use either a statically configured or dynamically learned default route. The default route matches all packets, so that if a packet does not match any other more specific route in the routing table, the router can at least forward the packet based on the default route.
    For example: ip route 0.0.0.0 0.0.0.0 s0/0/1