## Slide 1: DHCP and IP Networking on Hosts
Liu Cui

## Slide 2: Implementing and Troubleshooting DHCP
The DHCP process to lease an IP address use the following four messages between the client and server:
  Discover: Sent by the DHCP client to find a willing DHCP server
  Offer: Sent by a DHCP server to offer to lease to that client a specific IP address (and inform the client of its other parameters)
  Request: send by the DHCP client to ask the server to lease the IPv4 address listed in the Offer message.
  Acknowledgement: Sent by the DHCP server to assign the address, and to list the mask, default router, and DNS server IP addresses

## Slide 3: Implementing and Troubleshooting DHCP
DHCP clients, however, have a somewhat unique problem: they do not have an IP address yet, but they need to send IP packets. To make that work, DHCP messages make use of two special IPv4 addresses that allow a host that has no IP address to still be able to send and receive messages on the local subnet:
  0.0.0.0: An address reserved for use as a source IPv4 address for hosts that do not yet have an IP address
  255.255.255.255: The local broadcast IP address. Packets sent to this destination address are broadcast on the local data link, but routers do not forward them.

## Slide 4: Supporting DHCP for Remote Subnets with DHCP Relay
Network engineers have a major design choice to make with DHCP: Do they put a DHCP server in every LAN subnet, or locate a DHCP server in a central site?
Cisco routers can act as the DHCP server, so a distributed design could use the router at each site as the DHCP server.
With a centralized DHCP server, those DHCP messages that flowed only on the local subnet somehow need to flow over the IP network to the centralized DHCP server and back. To make that work, the routers connected to the remote LAN subnets need an interface subcommand: the ip helper-address server-ip command.

## Slide 5: Supporting DHCP for Remote Subnets with DHCP Relay
The ip helper-address server-ip subcommand tells the router to do the following for the messages coming in an interface, from a DHCP client:
  1. Watch for incoming DHCP messages, with destination IP address 255.255.255.255
  2. Change that packet’s source IP address to the router’s incoming interface IP address
  3. Change that packet’s destination IP address to the address of the DHCP server (as configured in the ip helper-address command)
  4. Route the packet to the DHCP server

## Slide 6: Information Stored at the DHCP Server
The DHCP server is actually software, running on some server OS. The DHCP server could be a piece of software downloaded for free and installed on an old PC. However, because the server needs to be available all the time, to support new DHCP clients, most companies install the software on a very stable and highly available data center.
The following list shows the types of settings the DHCP server needs to know to support DHCP clients:
  Subnet ID and mask
  Reserved (excluded addresses)
  Default router(s)
  DNS IP address(es)

## Slide 7: DHCP Server Configuration on Routers
Step 1: Use the ip dhcp excluded-address first last command in global configuration mode to list addresses that should be excluded
Step 2: Use the ip dhcp pool name command in global configuration mode to both create a DHCP pool for a subnet and to navigate into DHCP pool configuration mode. Then also:
  A. Use the network subnet-ID mask or network subnet-ID prefix-length command in DHCP pool configuration model to define the subnet for this pool.
  B. Use the default-router address 1 address 2… command in DHCP pool configuration model to define default router IP address(es) in that subnet.
  C. Use the dns-server address1 address2… command in DHCP pool configuration model to define the list of DNS server IP addresses used by hosts in this subnet.
  D. Use the lease days hours minutes command in DHCP pool configuration model to define the length of the lease, in days, hours, and minutes
  E. Use the domain-name name command in DHCP pool configuration model to define the DNS domain name.
  F. use the next-server ip-address command in DHCP pool configuration mode to define the TFTP server IP address used by any hosts (like phones) that need a TFTP server.

## Slide 8: IOS DHCP Server Verification
show ip dhcp binding: lists state information about each IP address currently leased to a client
show ip dhcp pool [poolname] : lists the configured range of IP addresses, plus statistics for the number of currently leased addresses and the high-water mark for leases from each pool
show ip dhcp server statistics: lists DHCP server statistics

## Slide 9: DHCP Troubleshooting
Step 1: If using a centralized DHCP server, at least one router on each remote subnet that has DHCP clients must act as DHCP relay agent, and have a correctly configured ip helper-address address subcommand on the interface connected to that subnet.
Step 2: If using a centralized IOS DHCP server, make sure the DHCP pool’s network commands match the entire network’s list of router interfaces that have an ip helper-address command pointing to this DHCP server.
Step 3: Troubleshoot for any IP connectivity issues between the DHCP relay agent and the DHCP server, using the relay agent interface IP address and the server IP address as the source and destination of the packets.
Step 4: Troubleshoot for any LAN issues between the DHCP client and the DHCP relay agent.

## Slide 10: Detecting Conflicts with Offered Versus Used Addresses
Although the DHCP server configuration clearly lists the addresses in the pool, plus those to be excluded from the pool, hosts can still statically configure addresses from the range inside the DHCP pool. In other words, no protocols prevent a host from statically configuring and using an IP address from within the range of addresses used by the DHCP server.
DHCP servers detect conflicts by using pings. Before offering a new IP address to a client, the DHCP server fist pings the address.If the server receives a response to the ping, some other host must already be using the address, which lets the server know a conflict exist.
DHCP clients detect conflicts by using ARP. When the DHCP client receives from the DHCP server an offer to use a particular IP address, the client sends an ARP request for that address. If another host replies, the DHCP client has found a conflict.

## Slide 11: Verifying Host IPv4 Settings
IP address and Mask Configuration
  ipconfig: Windows
  ifconfig: Linus and Mac OS