## Slide 1: Lecture 10a
The Network Layer (1): The Internet Protocol

## Slide 2: Internetworking
Before Internet: different packet-switching networks (e.g., ARPANET, IBM SNA, Ethernet, packet radio, etc.)
  Only nodes on the same network could communicate
Principal focus of Network Layer in protocol stack
How to allow independently owned and administered networks to interconnect?
Two nodes communicating across a “network of networks”…
  How to transport information through this heterogeneous mess ?
  This was one of the key drivers of the Internet in the 1980s
?
?

## Slide 3: The Internetworking Problem
Problems: heterogeneity and scaling
Heterogeneity:
  How to interconnect a large number of disparate networks ? ( different lower layers)
  How to support a wide variety of applications ? (different upper layers)
Scaling:
  How to support a large number of end-nodes and applications in this interconnected network ?

## Slide 4: Internet Solution to Internetworking
Network Layer
Gateways

## Slide 5: The Internet Solution …
Network layer gateways & global addresses
  Simple, application-independent, lowest denominator network service based on datagram based packet switching
Stateless gateways called “routers” can easily route around failures
Define a new protocol Internet Protocol(IP) and map all applications/networks to IP
  IP independent of lower layer network technology
IP
IP
IP
IP

## Slide 6: Switching Methods
Three general approaches to moving information through multi-node interconnected networks
  Circuit Switching
    Dedicates “network” resources, blocking, pay per minute
    Need signaling to teardown path when done
    Wastes the resources when the load is light
  Message Switching
  Packet Switching

## Slide 7: Message switching
General
  Transmission is one node at a time (entire path is not dedicated)
  Uses delay to mediate contention

## Slide 8: Packet switching
Similar in principal to message switching
  Uses delay to mediate contention
  Transmission is one node at a time
Messages broken into pieces called packets and each packet is transmitted one at a time
Supports
  Multiprocessing: Simultaneously transmits the previously received packet as it is receiving the next packet. Message switches cannot do this because they must receive the entire message before retransmitting it.
  Pipelining: Packets from same message can be in transit on multiple links simultaneously

## Slide 9: Circuit vs. Packet vs. Message Switching
Time
Packet 1
Packet 2
Packet 3
message
Circuit Switching
Message Switching
Packet Switching
Notes: Packet Switching obtains its benefit by multiprocessing. That is, it simultaneously transmits the previously received packet as it is receiving the next packet. Message switches cannot do this even if they are constructed to because they must receive the entire message before retransmitting it. If several separate messages are being transmitted in sequence, the message switch can multiprocess, but that does not help an individual message.

## Slide 10: Comparing switching techniques
Type | Contention mgt | Bandwidth | Delay components | Comments
Circuit | Blocking | Use only a slice of bandwidth, but all the time | Call setup Propagation Transmission | Call setup > 2* propagation
Message | Delay | Use full link bandwidth, but only for message | Queueing Propagation Transmission | Entire message received & transmitted at each node
Packet | Delay | Use full link bandwidth, but only for packet | Queueing Propagation Transmission | Each packet received & transmitted at each node

## Slide 11: Two ways for Packet switching
Connection Oriented (virtual circuit)
    Set up route between source and destination of communication
    All packets go on same route
    Can “reserve” or not - the resources on the route
      Source routing in IP?
Connection-less (datagram)
    Route each packet independently through the network
    No reserved resources – no guarantees of service quality

## Slide 12: Connection Oriented Service
Before data flows, two end hosts and intervening network components establish connection or virtual connection (VC)
Need signaling protocol to setup, maintain teardown VC
Each packet has VC ID in header – decision based on ID
  Used in ATM, frame-relay, X.25
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 13: Datagram (IP) networks
No call setup at network layer
Network components retain no state about end-to-end connections
  No network-level concept of “connection”
Packets forwarded using destination host address
  Packets between same source-dest pair may take different paths
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 14: Internet History
Evolved from ARPANet (Defense Department’s Advanced Research Projects Agency Network)
  ARPANet was developed in 1969, and was the first packet-switching network
  Initially, included only four nodes: UCLA, UCSB, Utah, and SRI
Key points
  ARPAnet/Internet was a general purpose network (i.e., was not optimized for a particular application)
  Used delay to mediate contention for resources
See: https://www.internetsociety.org/sites/default/files/GUIS-2012-Infographic.pdf

## Slide 15: Commercial Internet Use
ARPANet and NSF limited use to research and development
Early commercial use primarily information dissemination
Electronic transactions gradually moved to the Internet
WWW growth in 1990s led to increased direct sales over Internet
Growth has led to the expansion of data mining for target marketing

## Slide 16: Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  Residential, company and university ISPs
Access ISPs in turn must be interconnected.
  So that any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies
We take a stepwise approach to describe current Internet structure
RFC = Request for Comments – specifies internet related standards
  Developed by IETF – Internet Engineering Task Force
Slide modified from Kurose & Ross

## Slide 17: Functions of the Network layer
Transfer variable length data packets from a source network to a destination network via one or more networks
  Can optionally maintain different qualities of service (QoS)
    Term used to denote different application requirements
This task is called Routing
  Performed in the network by devices called Routers
Slide modified from Agrawal
Notes: IP focuses on the job of routing data, in the form of IP packets, from the source host to the destination host. IP does not concern itself with the physical transmission of data, instead relying on the lower TCP/IP layers to do the physical transmission of the data. Instead, IP concerns itself with the logical details, rather than physical details, of delivering data. In particular, the network layer specifies how packets travel end to end over a TCP/IP network, even when the packet crosses many different types of LAN and WAN links.

## Slide 18: Network and Link Layers
Look at the destination link (DL) address (how it changes)
Observe that the IP destination address does not change
Figure modified from Agrawal

## Slide 19: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Slide modified from Kurose & Ross
Recall from long long ago…

## Slide 20
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
Slide modified from Kurose & Ross

## Slide 21
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP
Slide modified from Kurose & Ross

## Slide 22
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C
Slide modified from Kurose & Ross

## Slide 23
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point
Slide modified from Kurose & Ross

## Slide 24
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
IXP
regional net
Slide modified from Kurose & Ross

## Slide 25
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network
Slide modified from Kurose & Ross

## Slide 26
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP
Slide modified from Kurose & Ross

## Slide 27: Connecting to the Internet
End users get connectivity from an ISP (internet service provider)
  Home users use dial-up, ADSL, cable modems, satellite
  Businesses use dedicated circuits connected to LANs
ISPs use “wholesalers” called network service providers and high speed (T-3 or higher) connections
Picture Source: http://mythman.typepad.com/.a/6a00d834520f3b69e20111688d4149970c-800wi

## Slide 28: Getting a Packet through the Network
Need addresses that are globally unique
  And some way to find them 
Need network devices that know about other network devices
Need a routing algorithm for finding a path
Need a mechanism for accommodating diverse networks
Many more details 

## Slide 29: IP Header
Slide modified from Agrawal

## Slide 30: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 31: IP Datagram Format
First Word purpose: info, variable size header & packet.
  Version (4 bits)
    IPv4 and IPv6
  Internet header length (4 bits): units of 32-bit words. Min header is 5 words or 20 bytes.
  Type of service (TOS: 8 bits): Reliability, precedence, delay, and throughput
    Not strictly used
  Total length (16 bits): header + data. Units of bytes. Total must be less than 64 kB.

## Slide 32: IP Header (Continued)
2nd Word Purpose: fragmentation
  Identifier (16 bits): Helps uniquely identify the datagram between any source, destination address
  Flags (3 bits): More Flag (MF):more fragments , Don’t Fragment (DF) ,Reserved
  Fragment offset (13 bits): In units of 8 bytes

## Slide 33: IP Header (Continued)
Third word purpose: demuxing, error/looping control, timeout.
  Time to live (8 bits): Specified in router hops
  Protocol (8 bits): Next level protocol to receive the data: for de-multiplexing.
  Header checksum (16 bits): 1’s complement sum of all 16-bit words in the header.
    Change header => modify checksum using 1’s complement arithmetic.

## Slide 34: Throughput
Mac OS X Definition: “the amount of material or items passing through a system or process”
IP Header has at least 5 x 32 = 160 bits (20 bytes)
Ethernet or WiFi header and CRC have their own bits
  WiFi has waiting times, backoff
TCP segment has its own header!
What is the application level data rate?
  Typically called throughput at various layers
    Bits/sec, packets/sec, packets/time slot, etc.

## Slide 35: Internet (IP) Addresses
When an organization connects to the Internet, it obtains a set of IP addresses for its computers
The current addresses consist of 32 bit binary numbers (IPv4)
  Theoretically up to 232 = 4.29 billion addresses
  IPV6 expands the address space
Routing each address uniquely would
  Require enormous routing tables and take a lot of time
  Solution: allocate addresses in blocks

## Slide 36: IP Addresses
Binary numbers are hard to remember, so use decimal equivalents
Divide decimal digit string into four sets of numbers separated by “dots”
136.142.185.57
Translate into binary
  Decimal to Binary
  Convert decimal to sum of binary exponents (0-7): 27=128, 26=64, 25=32, 24=16, 23=8, 22=4, 21=2, 20=1
  136=128+8= 27+ 23
  142=128+8+4+2= 27+ 23+ 22+ 21
10001000 10001110 10111001 00111001

## Slide 37: Original IP Address Blocks
Block sizes
  Big users (Class A) – 128 available, each for 16 million hosts
  Medium users (Class B) - 16,384 available, each for 65,000 hosts
  Small users (Class C) - 2 million available, each for 256 hosts
  Group of addresses assigned by ICANN: Internet Corporation for Assigned Names and Numbers

## Slide 38: IP Addresses
0
1
0
1
1
0
Class A
Class B
Class C
netid = 7 bits
hostid
netid = 14 bits, 214 = 16384
hostid
netid
hostid = 8 bits

## Slide 39: All Possible Valid Network Numbers

## Slide 40: Networks, Subnets & Addresses
Allows for the subdivision of networks within an organization
Each LAN can have a subnet number, allowing routing among networks
Host ID portion is partitioned into subnet and host numbers
Source: Forouzan

## Slide 41: Subnets
Host ID is divided in two parts
Subnet mask
32-bit number that tells the router how to separate the host address and the network address
Shown for
Class B
Boundary
determined
by Class
Often want 3 divisions:
subnet = front part of host id
=255.255.252.0
6 bits for Subnet
10 bits for host
How many possible subnets?
How many possible hosts?

## Slide 42: Subnet Mask Calculations
Subnet Mask: 32-bit number that tells the router how to separate the host address and the network address
Source: Stallings

## Slide 43: IP addressing: CIDR
CIDR: Classless Inter Domain Routing
  Address class is no longer uniquely identifiable from the address
  Subnet portion of address of arbitrary length
  Address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
Subnet part
Host part
200.23.16.0/23
verify

## Slide 44: IP addresses: How does a Network get one?
Q: How does a network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 45: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/30”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP – A+
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient
advertisement of address for routing information:
*
Notes: Two important facts about how IPv4 groups IP addresses:
All IP addresses in the same group must not be separated from each other by a router.
IP addresses separated from each other by a router must be in different groups

## Slide 46: A Summary of Router Forwarding Logic
1. Use the data-link Frame Check Sequence (FCS) field to ensure that the frame had no errors; if errors occurred, discard the frame.
2. Assuming that the frame was not discarded at Step 1, discard the old data-link header and trailer, leaving the IP packet.
3. Compare the IP packet’s destination IP address to the routing table and find the route that best matches the destination address. This route identifies the outgoing interface of the router, and possibly the next-hop router IP address.
4. Encapsulate the IP packet inside a new data-link header and trailer, appropriate for the outgoing interface, and forward the frame.

## Slide 47: IP Forwarding (I)
Source & Destination in same network (direct connectivity)
  Recognize that destination IP address is on same network
    Use subnet mask for this purpose
  Find the destination LAN (MAC) address
    Use Address Resolution Protocol (ARP) for this (later)
  Send IP packet encapsulated in LAN frame directly to the destination LAN address
    Encapsulation => source/destination IP addresses don’t change

## Slide 48: IP Forwarding (II)
B) Source & Destination in different networks (indirect connectivity)
  Recognize that destination IP address is not on same network.
  Look up destination IP address in a (L3 forwarding) table to find a match, called the next hop router IP address.
  Send packet encapsulated in a LAN frame to the LAN address corresponding to the IP address of the next-hop router.

## Slide 49: IP Forwarding: Example Scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
misc
fields
source
IP addr
dest
IP addr
data
datagram remains unchanged, as it travels source to destination
addr fields of interest here
routing table in A
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2

## Slide 50: IP Forwarding (Direct)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
* look up network address of B
* find B is on same network as A
* link layer will send datagram directly to B inside link-layer frame
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
misc
fields
223.1.1.1
223.1.1.3
data
  A,B are directly connected

## Slide 51: IP Forwarding (Indirect): 1
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
Starting at A, dest. E:
* look up network address of E
* E on different network
* routing table: next hop router to E is 223.1.1.4
* link layer sends datagram to router 223.1.1.4 inside link-layer frame
* datagram arrives at 223.1.1.4
continued…..
misc
fields
223.1.1.1
223.1.2.2
data
  A, E not directly attached

## Slide 52: IP Forwarding (Indirect): Step 2
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Arriving at 223.1.1.4, destined for 223.1.2.2
* look up network address of E
* E on same network as router’s interface 223.1.2.9
  router, E directly attached
* link layer sends datagram to 223.1.2.2 inside link-layer frame via interface 223.1.2.9
* datagram arrives at 223.1.2.2
misc
fields
223.1.1.1
223.1.2.2
data
network router Nhops interface
223.1.1 - 1 223.1.1.4
223.1.2 - 1 223.1.2.9
223.1.3 - 1 223.1.3.27
Dest. next