## Slide 1: Lecture 11a
The Transport Layer and Client-Server Applications

## Slide 2: Internet Protocol stack
Five layer stack built around Internet Protocol (IP) from IETF
Note multiple layer 1-2, and 5 protocols
Figure source: Agrawal

## Slide 3: It is Complex!
Many protocols at many layers
  Link layer - Ethernet & 802.11 are major
  Network layer and its “helper” protocols
    IP, ICMP, ARP, DNS, DHCP, ...
  Transport layer - TCP and UDP are major
Applications
  HTTP, SMTP, FTP, Telnet, IM, RSS feeds, Real, Web Services, SQL, Acrobat, Flash, Other Services,...

## Slide 4: Basic Operation
Transport Layer
Schematic of TCP/IP Operation

## Slide 5: The need for Transport Layer
The network layer (IP) sends packets of data to their correct destinations with best effort
  Packets may get lost in transit
  Therefore, network layer is not adequate for most applications to work correctly
What if the receiver cannot handle what the sender is transmitting?
  Flow control between hosts
The maximum packet size in IP is 65,536 bytes, so what happens if the application wants to send a file of size 5,000,000 bytes?
  Segmentation
Distinguish between applications on computers
Slide modified from Agrawal

## Slide 6: Internet transport protocols services
TCP service:
Connection-oriented: setup required between client and server processes
Reliable transport between sending and receiving process
Flow control: sender won’t overwhelm receiver
Congestion control: throttle sender when network overloaded
Does not provide: timing, minimum bandwidth guarantees
UDP service:
Unreliable data transfer between sending and receiving process
Does not provide: connection setup, reliability, flow control, congestion control, timing, or bandwidth guarantee

## Slide 7: But first … Applications
Write programs that
  run on (different) end systems
  communicate over network
  e.g., web server software communicates with browser software
Software not written for devices in network
  Network devices do not run user applications
  applications on end systems allows for rapid app development, propagation
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
Figure source: Kurose & Ross

## Slide 8: Application architectures
How do we bridge the gap between what users need/want and what the Internet provides?
What the Internet provides (refresher)
  IP provides best effort packet delivery
  MAC protocols provide connectivity to end user devices
The upshot of the reference model is that we only need to worry about the Transport layer!

## Slide 9: Application Architecture
Application layer
  Defines those elements of application functionality that need to be standardized
  Specific to particular application types
How is the app organized?
  Computer/processing/data/control
Stand Alone Applications
  Application resides on a single machine
  Networking limited to sharing data with other copies of the same application
  Example: Older Microsoft office programs
Centralized or Distributed Apps
  One of each (email & WWW, resp.) 

## Slide 10: Application architectures
Client-server
Peer-to-peer (P2P)
Hybrid of client-server and P2P

## Slide 11: Client-server architecture
server:
  “always-on” host
  permanent IP address
  server farms for scaling
clients:
  communicate with server
  may be intermittently connected
  may have dynamic IP addresses
  do not communicate directly with each other
client/server
Figure source: Kurose & Ross

## Slide 12: Pure P2P architecture
No always-on server
Arbitrary end systems directly communicate
Peers are intermittently connected and change IP addresses
Example: Gnutella
Highly scalable but difficult to manage
peer-peer
Figure source: Kurose & Ross

## Slide 13: Hybrid of client-server and P2P
Skype
  Voice-over-IP P2P application
  Centralized server: finding address of remote party
  Client-client connection: direct (not through server)
Instant messaging
  Chatting between two users is P2P
  Centralized service: client presence detection/location
    User registers its IP address with central server when it comes online
    User contacts central server to find IP addresses of buddies

## Slide 14: App-layer protocol defines
Types of messages exchanged,
  e.g., request, response
Message syntax:
  what fields in messages & how fields are delineated
Message semantics
  meaning of information in fields
Rules for when and how processes send & respond to messages
Public-domain protocols:
defined in IETF RFCs
allows for interoperability
e.g., HTTP, SMTP
Proprietary protocols:
e.g., Skype

## Slide 15: What transport service does an app need?
Data loss
Some apps (e.g., audio) can tolerate some loss
Other apps (e.g., file transfer, telnet) require 100% reliable data transfer
Timing
Some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
Bandwidth
Some apps (e.g., multimedia) require minimum amount of bandwidth to be “effective”
Other apps (“elastic apps”) make use of whatever bandwidth they get

## Slide 16: Transport service requirements of common apps
Application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video
interactive games
instant messaging
Data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
Bandwidth
elastic
elastic
elastic
audio: 5kbps-1Mbps
video:10kbps-5Mbps
same as above
> 100kbps
elastic
Time Sensitive
no
no
no
yes, 100’s msec
yes, few secs
yes, 100’s msec
yes and no

## Slide 17: Implications
Networking
  Connectivity requirements
    What links between components are necessary?
  Availability requirements
    Percentage of time application or data is available to users
  Performance requirements
    Response time requirements
    Throughput requirements
Application
  What functions belong in the (end user) application?
  What functions should be provided centrally?
More in IS 1071

## Slide 18: Application-to-Application Service
Hosts have many active apps 
Need app-to-app conn, not just host-to-host
1. Communication should be independent of network
Notes: End-to-end layers don’t see the infrastructure below them

## Slide 19: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 20: Communications Across a Network
Communicating processes typically have a client side and a server side
  Two processes on two different hosts that communicate using sockets
  A socket is like a door through which messages are sent and received
    Interface between the application process and the transport layer
Addressing a process
  Globally unique IP address
  Receive side port number

## Slide 21: Relationship to Application Layers
“Multiplexing”
Many app-to-app connections over
the same host-to-host connection

## Slide 22: Port addresses and multiplexing
On the sender side, the operating system assigns one of the free ports to an application that requires network connectivity
How do you know what port to connect to on the receiver side?
  On what port is the web server listening?
Standard ports
  Assigned by IANA: Internet Assigned Numbers Authority
Notes: Multiplexing by TCP and UDP involves the process of how a computer thinks when receiving data. The computer might be running many applications, such as a web browser, an email package, or an Internet VoIP application. TCP and UDP multiplexing tells the receiving computer to which application to give the received data.

## Slide 23: Processes and Sockets
Process
Transport
Layer
This is the application
This is TCP, UDP, etc.
Host Computer
Process
Transport
Layer
This is the application
This is TCP, UDP, etc.
Host Computer
Internet
Source: Computer Networking: A top down approach by Kurose and Ross
socket
Notes: Multiplexing relies on a concept called a socket. A socket consists of three things: (1) an IP address, (2) a transport protocol, (3) a port number
When you use three applications at the same time, three socket connections are open. Because a socket on a single computer should be unique, a connection between two sockets should identify a unique connection between two computers. This uniqueness means that you can use multiple applications at the same time, talking to applications running on the same or different computers.

## Slide 24: Application Addressing : Port Numbers
Clients use temporary port numbers
Servers use well-known port numbers

## Slide 25: Ports and Servers
Client contacts the server initially for all communications
  Server should react to the initial contact – it keeps listening to the port
    It has an initial “socket object” to accept connections
    It creates a new socket dedicated to a particular client after connection
  The initial socket object is what we loosely call as an “open” port
    It is really a half-open object
Popular standard protocols have assigned (fixed) port numbers
  Clients are aware of these numbers before they place a call (contact the server)
Notes: Port numbers are a vital part of the socket concept. Well-known port numbers are used by servers; other port numbers are used by clients. Applications that provide a service, such as FTP, Telnet, and web servers, open a socket using a well-known port and listen for connection requests. Because these connection requests from clients are required to include both the source and destination port numbers, the port numbers used by the servers must be well-know.
On client machines, where the requests originate, any locally unused port number can be allocated.

## Slide 26: Standard ports
Typically ports 1 – 1023 are reserved for defined services
  Applications may use the remaining port numbers 1024 – 65535
Common ports
  80 : web (http)
  25 : email (smtp)
  443: SSL (https)
  161: SNMP
To see list
  In Windows:
    C:/Windows/System32/drivers/etc/services
  In UNIX/ Linux
    /etc/services
Used ports displayed by netstat utility
Notes: The world wide web application exists through web browsers accessing the content available on web servers. Although it is often thought of as an end-user application, you can actually use WWW to manage a router or switch. You enable a web server function in the router or switch and use a browser to access the router or switch.
SNMP (Simple Network Management Protocol) is an application layer protocol used specifically for network device management. For example, Cisco supplies a large variety of network management products, many of them in the Cisco Prime network management software product family. They can be used to query, compile, store, and display information about a network’s operation. To query the network devices, Cisco Prime software mainly uses SNMP protocols.

## Slide 27: Port Numbers Continued
Port numbers by convention are low numbered
  Conventions are not always followed
  In UNIX and UNIX-like OSs, port numbers smaller than 1024 are privileged
    Only “root” can create these ports
    Remote systems were supposed to be able to trust the authenticity of these ports
Some standard port numbers
  Web server (http) – 80, (https) - 443;
  DNS – 53;
  Mail server (smtp) – 25; SSH – 22;
  Telnet server – 23; FTP – 20 and 21;
  POPv2 - 109, POPv3 - 110, IMAP - 143
Notes: The domain name system allows users to use names to refer to computers, with DNS being used to find the corresponding IP addresses. DNS also uses a client/server model, with DNS servers being controlled by networking personnel and DNS client functions being part of most any device that uses TCP/IP today. The client simply asks the DNS server to supply the IP address that corresponds to a given name.

## Slide 28: etc\services file
Show in Mac

## Slide 29: Transmission Control Protocol (TCP)
Reliable transport protocol
  IP is unreliable (or Best Effort)
  TCP takes an unreliable network and transforms it into a reliable connection for applications
Connection-oriented protocol
  Establish connection between link entities before data transfer
  Contrast with connectionless
  Defined in RFC 793 (Sep 1981)

## Slide 30: TCP functions
TCP corrects for the imperfections of IP
Therefore TCP has to perform many tasks
  Multiplexing
  Segmentation
  Reliability
  Connection establishment
  Flow-control

## Slide 31: TCP Segment
There are six flag bits
ACK - indicates its ACK field is valid
RST, SYN and FIN are used for connection set up and tear down
PSH - send data to higher layers right away
URG - there is some urgent data
Source port (16 bits)
Destination port
Sequence number
Acknowledgement number
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 32: TCP functions - multiplexing
Modern computers are capable of multi-tasking
  Including simultaneous communication tasks
TCP supports multiplexing by providing multiple port addresses within each host
  One communication channel per port
A network address and port address together is called a socket
  A pair of sockets uniquely identifies each connection

## Slide 33: TCP - segmentation
TCP allows IP to transfer arbitrarily large data blocks
  Accomplished by breaking data into segments (called called datagrams)
  A sequence number is assigned to each datagram
  Sequence numbers help receiver order datagrams even when received out of order
Sequence number of a TCP segment | = | sequence number of the previous segment + length of previous segment

## Slide 34: Sequence Numbers in TCP
Sequence and acknowledgment numbers are very important in TCP for reliable data transfer
The sequence number of a TCP segment tells the receiver how many bytes of data has been sent
  Example: the first TCP segment carries 320 bytes of data and the sequence number is 301, the next TCP segment will have a sequence number 621
The acknowledgment number tells the recipient what is the next expected byte number
  Example: the server receives 1000 bytes from the TCP segment with sequence number 235 - it has received bytes numbered 235 through 1234. So its sets the ACK number to be 1235

## Slide 35: TCP functions - reliability
Datagrams may get seriously damaged during transmission
  If datagrams are further fragmented by IP, some IP fragments may get lost during transmission
    These errors cannot be detected by Ethernet
  Such damage is corrected by adding a checksum to each datagram and comparing it at the receiver
    Damaged datagrams are discarded and retransmitted by sender since no ACK is received
Notes: TCP provides for reliable data transfer, which is also called reliability or error recovery. To accomplish reliability, TCP numbers data bytes using the Sequence and Acknowledgement fields in the TCP header. TCP achieves reliability in both directions, using the Sequence Number field of one direction combined with the Acknowledgment field in the opposite direction.

## Slide 36: Error Control (Retransmission)

## Slide 37: TCP functions - segmentation
Advantages
  Errors are less likely in smaller segments
  Less retransmission if error is introduced in a segment
  Easier for routers to hold segments in memory if onward route is busy
Disadvantages
  More computations in sending and receiving
  Duplicates are possible and must be detected

## Slide 38: TCP Connection Establishment
TCP uses error detection and correction
TCP uses sliding window flow control
These occur between the two hosts, not with the network
Notes: This three-way connection establishment flow (also called a three-way handshake) must complete before data transfer can begin. The connection exists between the two sockets, although the TCP header has no single socket field. Of the three parts of a socket, the IP addresses are implied based on the source and destination IP addresses in the IP header. TCP is implied because a TCP header is in use, as specified by the protocol field value in the IP header. Therefore, the only parts of the socket that need to be encoded in the TCP header are the port numbers.

## Slide 39: TCP Connection Management
Client wants to initiate connection to server
  It sends a special TCP segment to the server with the SYN bit set to 1
  The initial sequence number is say client_isn
  This is called a SYN segment
Server receives the SYN segment
  It allocates buffers and variables to the connection and replies
  Reply has SYN = 1, acknowledgment number = client_isn +1
  Sequence number is server_isn
  This is called a SYNACK segment
Connection is completed
Three-way Handshake
Notes: TCP signals connection establishment using 2 bits inside the flag fields of the TCP header. Called the SYN and ACK flags, these bits have a particularly interesting meaning. SYN means synchronize the sequence numbers, which is one necessary component in initialization for TCP.

## Slide 40
Details of Connection
Management

## Slide 41: TCP States - Client and Server

## Slide 42: Connection Termination
The graceful method to terminate the connection is to use the FIN field followed by ACK
  In this case, either the client or the server will first send a TCP segment with the FIN bit set
  The receiving host will ACK the FIN
  This process closes half the connection - it has to be repeated by the receiving host
The abrupt method of closing the TCP connection is for either the client or the server to send an RST (reset) segment
  This aborts the TCP connection and no further communications take place between the hosts

## Slide 43: Connection Termination

## Slide 44: TCP functions – flow control
If the receiver is slow, it will not be able to process the packets reaching it fast enough
Therefore, TCP enables the receiver to limit the sender’s data rate
If sender is slow, it only tests the patience of receivers
  There is no packet loss
  Also, sender is already transmitting at max possible rate
Notes: TCP implements flow control y using a window concept that is applied to the amount of data that can be outstanding and awaiting acknowledgment at any one point in time. The window concept lets the receiving host tell the sender how much data it can receive right now, giving the receiving host a way to make the sending host slow down or speed up. The receiver can slide the window size up and down to change how much data the sending host can send.

## Slide 45: Stop and Wait Flow Control

## Slide 46: TCP functions – flow control
TCP flow control is accomplished by returning a “window” with every ACK
“Window” indicates how many bytes of data the sender may transmit before receiving any more ACK
  The window size increases with every correct packet
  This continues until a NAK is received, when the window size becomes “1”
  Thus, the throughput follows a sawtooth pattern
time
Throughput

## Slide 47: Stop and Wait with window size

## Slide 48: Sliding window
Flow control is the regulation by the receiver of the amount of data the sender may send
Creates a “sliding window” at the sender
Packets that have received permission for transmission are within the window
Window slides through the data as receiver acknowledges packets or modifies window size

## Slide 49: Sliding window

## Slide 50: Sliding Windows
Normally a data link layer concept.
Our interest is understanding the TCP mechanism at the transport layer.
Each frame is assigned a sequence number: SeqNum.
The sender maintains three variables: send window size (SWS), last ACK received (LAR), and last Frame sent (LFS).

## Slide 51: Sender Variables
SWS :: the upper bound on the number of outstanding frames (not ACKed) the sender can transmit.
LAR :: the sequence number of the last ACK received.
LFS :: the sequence number of the last frame sent.

## Slide 52: Sender Invariant
LFS – LAR <= SWS
LAR
LFS
<=SWS

## Slide 53: Sender Window
An arriving ACK  LAR moves right 1
 sender can send one more frame.
Associate a timer with each frame the sender transmits.
Sender retransmits the frame if the timer times out.
Sender buffer :: up to SWS frames.

## Slide 54: Receiver variables
Receiver window size (RWS) :: the upper bound on the number of out-of-order frames the receiver is willing to accept.
Largest acceptable frame (LAF) :: the sequence number of the largest acceptable frame.
Last frame received (LFR) :: the sequence number of the last frame received.

## Slide 55: Receiver Invariant
LAF – LFR <= RWS
LFR
LAF
<=RWS

## Slide 56: Receiver Window
When a frame arrives with SeqNum:
  If (SeqNum <= LFR or SeqNum > LAF)
  the frame is discarded because it is outside the window.
  If (LFR < SeqNum <= LAF)
  the frame is accepted.

## Slide 57: Receiver ACK Decisions
SeqNumToAck :: largest sequence number not yet ACKed such that all frames <= SeqNumToAck have been received.
Receiver ACKs receipt of SeqNumToAck
  and sets
  LFR = SeqNumToAck
  LAF = LFR + RWS
  SeqNumToAck is adjusted appropriately!

## Slide 58: TCP Sliding Windows
In practice, the TCP implementation switches from packet pointers to byte pointers.
Guarantees reliable delivery of data.
Ensures data delivered in order.
Enforces flow control between sender and receiver.
The idea is: the sender does not overrun the receiver’s buffer.

## Slide 59: Receiver’s Advertised Window
The big difference in TCP is that the size of the sliding window size at the TCP receiver is not fixed.
The receiver advertises an adjustable window size (AdvertisedWindow field in TCP header).
Sender is limited to having no more than AdvertisedWindow bytes of unACKed data at any time.

## Slide 60: TCP Flow Control
The discussion is similar to the previous sliding window mechanism except we add the complexity of sending and receiving application processes that are filling and emptying their local buffers.
Also we introduce the complexity that buffers are of finite size without worrying about where the buffers are stored.
        MaxSendBuffer
        MaxRcvBuffer

## Slide 61: TCP Flow Control
Receiver throttles sender by advertising a window size no larger than the amount it can buffer.
On TCP receiver side:
LastByteRcvd - LastByteRead<=MaxRcvBuffer
to avoid buffer overflow!

## Slide 62
TCP receiver advertises:
AdvertisedWindow = MaxRcvBuffer -
(LastByteRcvd - LastByteRead)
i.e., the amount of free space available in the receiver’s buffer.
TCP Flow Control

## Slide 63
The TCP sender must adhere to AdvertisedWindow from the receiver such that
LastByteSent – LastByteAcked <= AdvertisedWindow
or use EffectiveWindow:
EffectiveWindow = AdvertisedWindow – (LastByteSent – LastByteAcked)
TCP Flow Control

## Slide 64
Sender Flow Control Rules:
EffectiveWindow > 0 for sender to send more data.
LastByteWritten – LastByteAcked <= MaxSendBuffer
equality here  send buffer is full!!
 TCP sender process must block the sender application.
Animation link
TCP Flow Control

## Slide 65: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
No connection establishment: (which can add delay)
Simple:
no connection state at sender, receiver
Small header
No congestion control:
UDP can blast away as fast as desired
Notes: UDP provides a service for applications to exchange messages. Unlike TCP, UDP is connectionless and provides no reliability, no windowing, no reordering of the received data, and no segmentation of large chunks of data into the right size for transmission. However, UDP provides some functions of TCP, such as data transfer and multiplexing using port numbers, and it does so with fewer bytes of overhead and less processing required than TCP. UDP data transfer differs from TCP data transfer in that no reordering or recovery is accomplished. Applications that use UDP are tolerant of the lost data, or they have some application mechanism to recover lost data. For example, VoIP uses UDP because if a voice packet is lost, by the time the loss could be noticed and the packet retransmitted, too much delay would have occurred, and the voice would be unintelligible. Also DNS requests use UDP because the user will retry an operation if the DNS resolution fails. As another example, the Network File System (NFS), a remote file system application, performs recovery with application layer code, so UDP features are acceptable to NFS.

## Slide 66: UDP
Used for streaming multimedia apps, VoIP
  loss tolerant
  rate sensitive
other UDP uses
  DNS
  SNMP
reliable transfer over UDP: add reliability at application layer
  application-specific error recovery!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 67: Discussion
TCP
  Provides a reliable, connection-oriented data transfer
  Uses much more protocol overhead (at least 20 bytes)
UDP
  Provides unreliable, connectionless data transfer
  Uses much less protocol overhead (8 bytes)
Both use encapsulation
  Application messages and overhead are considered “Data” to TCP and UDP
  They do not recognize them and do not process them

## Slide 68: Example of Encapsulation
TCP Header
Request Line
Headers
Request Body
TCP Header
Request Line
Headers
Request Body
IP Header
TCP Header
Request Line
Headers
Request Body
TCP Header
IP Header
TCP Header
Request Line
Headers
IP Header
CRC
Eth. Header
Request Body
TCP Header
IP Header
Eth. Header
CRC
IP Packets sent
Ethernet Frame
TCP Segment
Original HTTP Request
Notice there are TWO segments

## Slide 69: TCP/ IP technologies by layer

## Slide 70: Summary: Transport Layer
Provides services for the transfer of data between end points independent of the physical network infrastructure.
Can provide end-to-end error recovery and flow control, security

## Slide 71: Summary
Transport Layer
  Why necessary
TCP
  Format
  Segments
  Sliding Window Flow/Error control  reliable
UDP
  Format
  Unreliable
  Real-time applications
Ports