## Slide 1: Lecture 1b
Networking: The Big Picture

## Slide 2: Tangled and Intricate
Grasping the details of networking is not simple
There are too many terms, acronyms, concepts, ideas, relations, similarities, differences
We will start slowly and build up our understanding

## Slide 3: What we will do today
Look at a few examples, that have similarities and differences
Idea is to provoke some thoughts and questions about how networks of today operate
  What needs to be in place to allow applications, devices, and humans to communicate?
  What problems can we anticipate?
  What quantitative metrics should we consider to evaluate the “performance” of networks?

## Slide 4: Big Picture
Alice wants to send a greeting card to her grandmother. How does this work?
Alice wants to call Bob using (gasp!) the landline. How does this work?
Alice wants to browse Amazon.com to buy a book. What needs to happen to make this work?

## Slide 5: Sending a Greeting Card (1)
Goes to store, gets card
Writes card for Grandma
Calls Mom for address!
Fixes stamp, Drives
Mails card
May have special terms for grandma
Content comes from here
Grandma doesn’t have e-mail or facebook!
Standard Vs Non-standard sizes matter
Alice

## Slide 6: Sending a Greeting Card (2)
Truck picks up the mail from mail box
  Also get’s other mail from other folks
Mail goes to “sorting facility”
  Mail to the same zip code go together
Mail is flown to destination
  Perhaps trucked to destination post-office
Mail is sorted by route and delivered by mailman (delivery van)
Grandma picks up mail, opens greeting card first while discarding junk mail
See: http://en.wikipedia.org/wiki/United_States_Postal_Service for details

## Slide 7
Source: http://upload.wikimedia.org/wikipedia/commons/e/e7/USPS_mail_flow_through_national_infrastructure.svg

## Slide 8: Things to note
Acronyms! – It is a matter of language
There are different transportation methods
  Cars, trucks, airplanes, delivery vans
  Differences: Drop-off and Delivery Versus Sorting and Routing
There are different types of packages
  Large, medium, small boxes
There are different types of services
  First-class, bulk, certified, express, priority
Addressing and envelope are important
  Follows a standardized format
  Alice had to find the address!

## Slide 9: Things to note (2)
Recall UPS’s delayed Christmas deliveries
Bottleneck due to limited capacity (number of flights)
  Read articles
  What if UPS had leased twice the number of aircrafts? Would they all be utilized?
  Toys Vs perishable goods (QoS)
Bottlenecks can occur in many places due to many reasons
  Weather, trucks, flights, people, machines, sorting, …

## Slide 10: Big Picture
Alice wants to send a greeting card to her grandmother. How does this work?
Alice wants to call Bob using (gasp!) the landline. How does this work?
Alice wants to browse Amazon.com to buy a book. What needs to happen to make this work?

## Slide 11: Voice Call on Land-line (1)
Looks up her contacts for
Mom’s phone number
Lifts the phone, gets
dial-tone
Dials the phone number
for her mom
Dial-tone indicates phone is working
“Address” here is the phone number
Dialing the number tells the “network” who should be reached
“Ring” tell’s Alice that her Mom’s phone may be ringing
Alice
Hears the phone “ring”
Rring

## Slide 12
Source: http://madebyjoel.com/wp-content/uploads/2010/04/Made-by-Joel-Tin-Can-Phones-2.jpg

## Slide 13: Voice-Call on Land-line (2) (simplified)
Alice
Dedicated line to Alice
To Inter-exchange Carrier
Slide modified from those provided by the author of the textbook
A dedicated “circuit” is set up from the IXC to Alice’s Mom
OR Central Office

## Slide 14: Voice Call on Landline (3)
The “trunk” from the central office to the Inter-exchange Carrier “multiplexes” many voice calls
  Compare with many pieces of mail and packages to the same state being flown over a plane
“Resources” are dedicated to a voice call
  It appears as if there is an exclusive “wire” between Alice’s phone and her grandmother’s phone
  The “wire” is created by “switches” in the phone network using the phone number
    It takes time to set up the call
  Such a connection is called “Circuit Switched”
    We will revisit “switching” later

## Slide 15: Circuit switched voice call (simplified)
…
…
Central
Office
Alice
Central
Office
Tandem
Office
IXC – A’s
POP
IXC – B’s POP
IXC-A’s Network
IXC-B’s Network
Tandem
Office
IXC – A’s
POP
IXC – B’s POP
Central
Office
POP = Point of Presence
Circuit

## Slide 16: Big Picture
Alice wants to send a greeting card to her grandmother. How does this work?
Alice wants to call Bob using (gasp!) the landline. How does this work?
Alice wants to browse Amazon.com to buy a book. What needs to happen to make this work?

## Slide 17: Browsing Amazon.com (1)
Boots her computer and
Opens browser
Types
http://www.amazon.com
Browser “loads” page
Alice
Browser is called the “client” software
“www.amazon.com” is the identity of “server”(s)
Is this magic??

## Slide 18: Questions
How does the browser know what and where amazon.com is?
How does it “communicate” with amazon.com?
  How is it connected to the Internet?
What if Alice is also browsing cnn.com at the “same” time?
How does the browser know if it has received the elements of the html page correctly?

## Slide 19
Slide modified from Agrawal
“Packet switching” – to be revisited

## Slide 20: What is a Communications Network?
A system of interconnected devices and the underlying infrastructure that enable the exchange of electronic information (analog or digital)
Components
  Electronic communication devices
    PCs, phones, tablets, sensors, laptops, servers, etc.
  Network Devices
    Hubs, routers, cross-connects, base stations, firewalls, databases, name servers, etc.
  Communication links
    Coaxial cable, twisted pair cable, wireless, etc.
  Services
    Phone calls, video, web, software applications, etc.

## Slide 21: Networks are part of IT infrastructure
Information Technology (IT) or Information and Communications Technology (ICT) infrastructure components
  Computational end/user devices
  Networks
    Telephone networks (wired and wireless)
    Internet and access networks (wired and wireless)
    Satellites
  Links
Heterogeneous components/technology
Variety of services provided
  Web, voice, video, SCADA, email, SMS
Compare with package sizes and content with postal service

## Slide 22: Computational/User Devices
Continuum
  Sensors/embedded controller
  Handhelds (tablets, cellphones)
  PCs/Workstations
  High data rate sensors (e.g., radar)
  Video cameras
  Servers
  Databases
  Etc.
Heterogeneous devices
  Features, Functions, OS platforms different
  Security vulnerabilities and capabilities differ

## Slide 23: Internet of “everything”
The Philips “Hue”
The Nest “Protect”

## Slide 24: Types of Networks – One Classification
Based on geographical size
  Access Networks
    LANs, Campus, Residential networks, etc.
  Metropolitan Networks (Metro Nets)
    Interconnection of central offices, POPs, corporate locations in a city, campus backbone network
    Higher bandwidth, may include leased communication links
  Wide Area Networks (WANs) or Long Haul Networks
    Private and Public Backbone networks (Level3, AT&T)
    Content Delivery Networks (Akamai)
    Corporate virtual private network over common infrastructure
Mail delivery
Local loop for landline call

## Slide 25: Yet another analogy: Airline inter-hub
A traveler from West Chester, PA needs to visit Naples, Italy.
  An airport shuttle collects people going to the airport
  A regional “commuter” jet brings him/her to JFK airport in New York City
  At NYC, people from all over East Coast board a well-filled 747 non-stop flight to Rome, Italy
  From Rome, a regional jet takes traveler to Naples
  Airport shuttle drops travelers at their hotels in Naples
Pattern:
  Access - Transport - Access
An optical fiber wavelength is the “747” (long-haul)
Multiplexing in the access and metro transport stages (switches, routers) are the regional airlines
Efficient solutions in airlines, shipping, and telecommunications industry all have this basic repeated structure

## Slide 26
Backbone or Core
Central Offices
Metro Area 3
Access
Typical Wired Network Structure
Feeder Network
Metro Area 2
Metro Area 1
Metro Area N
Current Trends
Core ~ Mesh
Metro ~ Ring
Access ~ Tree

## Slide 27: Network Types Again
ACCESS: Twisted pair, T1, DSL, Cable Modem, WLAN, cellular, Fiber to Curb , Ethernet, etc.
Networks have varying technology, components and protocols depending on size!
METRO: SONET, ATM, MPLS, Carrier Ethernet, Frame Relay, WiMAX, point to point microwave, free space optical, etc
WAN: Cross connects, routers, etc, DWDM, MPLS, IP, etc, SIP, BGP, OSPF etc,
Notes: You all know what public networks look like. There is the access network, the metropolitan network, and the long haul networks. We are mostly focused on long-haul networks: Composed of very long fibre routes on which fibre cuts can be quite frequent. Also, the amount of traffic carried by these fibres is very high and therefore survivable is a big concern.

## Slide 28: Wireless Networks
Wireless Networks have another set of technologies and protocols!

## Slide 29: Telecom and Networking Industry is Regulated!
Unlike other components of IT
Regulatory bodies have a hierarchy
International Telecommunications Union (ITU)
  ITU is part of the United Nations
  Worldwide coordination/ standardization (e.g., telephone numbers)
  Allocation (e.g., satellite slots)
Federal Communications Commission (FCC) in the US
  Regulates wireless spectrum (bands, licenses, power levels, etc,)
  Long distance voice
  Cable,
  Satellite, etc.

## Slide 30: Telecom and Networking Industry Standardization
Heavy emphasis on standardization (interoperability, $)
Standards bodies include
  International Telecommunications Union
    Optical networking, telephony, cellular
  Internet Engineering Task Force (IETF)
    Internet protocols and enhancements
  Institute for Electrical and Electronic Engineers (IEEE)
    Ethernet, 802.11 WiFi
  European Telecommunications Standards Institute (ETSI)
    GSM, DSL
  3rd Generation Partnership Project (3GPP)
    UMTS, LTE, LTE-Advanced

## Slide 31: Enterprise Networking
Adopt an enterprise/business view of networking
  Network/communication infrastructure enables distributed applications
    Web, email, voice, instant messaging, video, e-commerce, file sharing, cloud computing, etc.
    Referred to as “unified communications” today
  Focus on communication services provided to apps
    Connectivity and performance

## Slide 32: Business Goals
Identify overall business goal of network
  What will the network be used for? Mission critical uses?
  How does the enterprise think the network will improve their business practices?
  What is the criteria to be used to judge the network success/failure?
Typical business goals (may not be realistic!)
  Increase revenue and profit
  Shorten product development cycles/improve corporate communications
  Provide new services/Modernize out-dated technologies
  Reduce network costs
  Make more data available to more people
  Improve network security and reliability

## Slide 33: Business Constraints
Organizational Politics and Policies
  Who will manage/run network
  What are the companies policy on suppliers, platforms, vendors etc.
  Open vs. proprietary solutions?
  Security issues
Budget and Staffing Constraints
  Cost will often limit network options
  Staff abilities may determine some of network choices
  Outsourcing vs. In House?
  Scheduling
Technical goal is to operate a network that meets users’ requirements + some they may not know they need.
  Scalability
  Availability
  Network Performance
    Utilization, Throughput, Delay
    Delay Jitter Packet Loss Call blocking
  Security
  Manageability/Interoperability
  Affordability $$