## Slide 1: Lecture 2a
Protocols and Layers

## Slide 2: So far and what next…
We described a hierarchy of network types based on their geographical service area
  Access, metro, long-haul
At a high level, we looked at three communication scenarios
  Greeting card, landline phone call, browsing Amazon.com
What all happens to make the browser display the web page?
  We look at the idea of protocols and layering in this context

## Slide 3: The Network Core
Mesh of interconnected routers or switches
The fundamental question: how is data transferred through net?
  Circuit switching: dedicated circuit per call: telephone networks
  Packet-switching: data sent through nework in discrete “chunks”
[Circuits: network resources are chopped up in units of “circuits”
Packets: data is chopped up in units of “packets”]
Figure from Kurose & Ross

## Slide 4: Revisiting the Landline Voice Call – Circuit Switching
Resources are “dedicated” for the duration of the voice call
A circuit is an electronic closed-loop path among two or more points
Circuit switched networks typically bill by the minute
Telegraph
Slide modified from Agrawal

## Slide 5
Source: http://media.treehugger.com/assets/images/2013/07/elon-musk-hyperloop.jpg.662x0_q100_crop-scale.jpg
Elon Musk and the Hyperloop

## Slide 6: Multiplexing
Combines multiple flows of information on a common transmission medium
The cost of the transmission medium is excessive
  Laying a highway is very expensive
  Digging to lay cables is also expensive
Can the same cable carry many communication flows? If so how?
  Imagine laying 200 cables to support 200 TV channels

## Slide 7: Switching
Switching
  Reduce the number of resources
  Think of a “shared” road, but still dedicated at any given time
  What happens if a user E is added to the systems below?
How about (near) simultaneous communications?
Slide modified from Agrawal
How many wires?
Notes: Multiplexing
  One wire carries multiple signals
  In 1874, the quadruplex telegraph developed by Thomas Edison transmitted two messages in each direction simultaneously, for a total of four messages transiting the same wire at the same time
Circuit switching
  One wire connects to multiple destinations
  March 10, 1891, Strowger switch patented
    Tampa connection - Buried in St. Pete - http://en.wikipedia.org/wiki/Almon_Strowger

## Slide 8: Approaches to switching
Circuit Switching
Packet switching (Virtual circuit)
Packet Switching (Datagram)
1st
Notes: Fig OK (stallings)

## Slide 9: Circuit Switching
a  b
Illustrates a
“local call”
c  d
Illustrates a
“long distance call”
Notes: Fig OK

## Slide 10: Circuit switching towards packet switching
Over 100 years of Circuit Switched Networks
Slide modified from Agrawal

## Slide 11: Why Packet Switching?
Increase in interactive data traffic (as opposed to voice traffic)
  Increased “burstiness” of data (high ratio of peak usage to mean usage)
  Example: Typical browsing behavior
Packet switching enables efficient utilization of communication links
  Averages the needs of a large numbers of users
  Aggregation and the law of large numbers
  3-100 times more efficient than circuit switching
Computing cost Vs communication cost
  Uses complete bandwidth
Eliminates single points of failure in data communication systems
Slide modified from Agrawal

## Slide 12: Packetization overview
Packetization is
  Breaking down user data into small segments
  Packaging these segments appropriately so that they can be delivered and reassembled across the network
  Circuit switching sends a continuous stream of data
Each segment or packet has two parts
  Data to be delivered
  “Overhead” required for successful delivery and integration with other packets
Slide modified from Agrawal
User Data
Seg
Seg
Seg
1
2
3
1
Header

## Slide 13: Packets analogy
Slide modified from Agrawal
Source Address
Destination Address
Other Info
PAYLOAD
In the end, these are all “bits”

## Slide 14: Packetization in retail
Ikea example
Priority mail example
  Postal mail is similar to packet switching in some respects
Slide modified from Agrawal

## Slide 15: Packet Switching aka “Routing”
Datagrams: Each packet is treated independently
Virtual circuit: A “path” is established
before any packets are sent
Packets:
Notes: Fig OK

## Slide 16: Approaches to switching
Circuit Switching
Packet switching (Virtual circuit)
Packet Switching (Datagram)
2nd
Notes: Fig OK (stallings)

## Slide 17: Packet Switching using datagrams
Successive packets may be
routed along different paths
And, may arrive out of order
Called “Routing”
(Layers 2 & 3) 
& these nodes
are called “Routers”

## Slide 18: Approaches to switching
Circuit Switching
Packet switching (Virtual circuit)
Packet Switching (Datagram)
3rd
Notes: Fig OK (stallings)

## Slide 19: Packet Switching using virtual circuits
1st, select route
for all packets
All packets are
routed along this path
And arrive in order

## Slide 20: Packet Switching vs Circuit Switching
Data transport over circuit-switch channels
  Circuit is unused when there’s no traffic
    Most of the time, if traffic is bursty (key strokes, file transfers)
    About 2/3 of the time for (half-duplex) voice
  End points must transmit/receive at constant fixed speed, limiting variety of devices that can be connected *(modem)
  Congestion  calls are blocked (Mother’s Day)
Data transport using packet switching
  Transmission medium is more efficiently used
    Can send packets from several users over same link *(mux)
  Devices that transmit at different speeds can communicate with each other
  Priority can be given to certain packets
  Congestion  packets delayed, but accepted *(overflow)
*Over-simplified

## Slide 21: Analysis
Circuit switching
  Good for applications that cannot tolerate delay
  Contention resolution by blocking
  Can be inefficient for bursty traffic
  Efficient if app market justifies custom network
Packet switching
  Large messages can result in long delays  Packets
  More efficient for bursty traffic
  Contention resolution by delay (with some loss)
  Commonly used in modern data networks

## Slide 22: Comparison

## Slide 23: Circuit Switching Again
Prior to communications, the “network” establishes the circuit (users not connected all the time)
  Call Establishment
The circuit takes up resources
  Bandwidth (time slots, frequency chunks) (what is bandwidth?)
The performance (e.g., delay) is predictable once the circuit is established
  Imagine having a dedicated road, truck, gasoline and driver to carry a package to a destination
Resources are typically underutilized and wasted
  Train tracks and hyperloops??
Performance metric is “call blocking”

## Slide 24: Bandwidth
Computer Science: a measurement of bit-rate (bit/s, kbit/s, Mbit/s, Gbit/s, etc.)
Wireless communications: measured in Hertz.
figure from: http://www.sengpielaudio.com/calculator-bandwidth.htm

## Slide 25: Revisiting Browsing Amazon.com
Boots her computer and
Opens browser
Types
http://www.amazon.com
Browser “loads” page
Alice
Browser is called the “client” software
“www.amazon.com” is the identity of “server”(s)
Always on!

## Slide 26: Questions
How does the browser know what and where amazon.com is? (Addressing)
How does it “communicate” with amazon.com? (Routing & protocols)
  How is it “always connected” to the Internet?
What if Alice is also browsing cnn.com at the “same” time? (Multiplexing)
How does the browser know if it has received the elements of the html page correctly? (Error control)

## Slide 27
Slide from Agrawal

## Slide 28: Packet switching
Routing data using “addressed” packets so that a “channel” is occupied only during the transmission of the packet
Packet switches are called routers
  Routers are devices used to interconnect two or more networks
Network resources are allocated (or used) as needed
Packet switched networks typically bill by the MB
Performance metrics are delay, jitter, throughput, packet loss rate
First packet transmission occurred on Oct 29, 1969, in California
Slide modified from Agrawal
Network 1
Network 2
Router

## Slide 29: Revisiting Greeting Card Scenario
Alice writes greeting card to grandmom
Grandmom reads greeting card
Alice puts it in envelope
Grandmom removes from envelope
Alice drops envelope in mailbox
Grandmom retrieves envelope from mail
Mailman picks up the mail from box
Mailman delivers mail to mailbox
Truck carries mail to post office
Truck carries mail from post office
Mail gets sorted
Mail gets sorted
Transport
There is a one-to-one correspondence
between layers in the two end points
There is a structured “flow”
between layers at each end

## Slide 30: Layering
Arranging functionality in a hierarchical manner
Lower layers provide functions and services that support the functions and services of higher layers
  Later: How we create and process packets
Example (corporate)
  VPs help CEOs reach their goals
  Managers help VPs reach their goals
  Workers work with tools and machines help managers reach their goals
We will see that there are so called “protocol layers” in computer networks
Slide modified from Agrawal

## Slide 31: Layering examples
Example (software)
  Computer applications delegate many tasks to operating systems
  Operating systems delegate tasks to “drivers” for execution
Slide modified from Agrawal
Revisit layering this week

## Slide 32: Layering in packet switched networks
Figure from Agrawal shows a simplified view of layering
We will use this figure occasionally to put things in context
Applications
Network Protocol Stack

## Slide 33: Processes
Software programs run as processes in an operating system
In Unix like operating systems (Mac OSX or Linux) you can use the ps command (process status) to list the processes
In Windows, you can use the task manager to look at the processes
process
TCP with
buffers,
variables
socket
host or
server
process
TCP with
buffers,
variables
socket
host or
server
Internet
controlled
by OS (kernel)
controlled by
app developer
Figure modified from Kurose and Ross

## Slide 34
Somewhere in this list of processes will be an instance of the browser that Alice is using
Say: firefox
It has a “process identifier”
Client Process

## Slide 35: Networked Applications
Processes on computers can communicate
  Communicate = exchange some commands, responses, data
If the processes are on the same end-host, they use “inter-process communications”
  Rules for exchanging data are based on the operating system
If the processes are on different hosts, they have to communicate over a network
  Maybe different operating systems
  Use messages to communicate
  Sending process sends a message, receiving process picks up the message

## Slide 36: Client and server processes
Alice’s browser is a client process running on her computer
It communicates with a server process that is running somewhere on some machine in Amazon.com’s network
Client initiates the contact (through the URL)
Server responds to the contact
  It has information about the client in the message that the client sends to the server

## Slide 37: Sockets
Programming interface used by a process to send and receive messages
  Like the door to a house
Sending process sends the message to the socket
  Assumption: There is something outside the door to transport the message to the door of the receiving process
At the door of the receiving process (socket), the message is received and pushed to the process
Application developer has little control over what is outside the door, only controls the process
  Can select from a set of “transport” protocols and some parameters
So what is a protocol?

## Slide 38: Protocols
Mac OS X Dictionary
  “the accepted or established code of procedure or behavior in any group, organization, or situation: what is the protocol at a conference if one's neighbor dozes off during the speeches?”
  “a set of rules governing the exchange or transmission of data between devices”
Recall
  Processes have to exchange data
  They send and receive messages
  The messages should follow some set of rules, so that the processes can recognize what is happening

## Slide 39: Example of Protocol
There is a sending and receiving of messages towards accomplishing something
The rules are there to make sure the communicating parties understand each other
Alice
Bob
Hello!
Én nem beszélek
angolul
???
Alice
Bob
Hello!
Hi. What can I
do for you?
Do you know where
I can find Dr. K?
time

## Slide 40: Example of Communication Protocol
Process uses TCP – transmission control protocol
TCP carries the request for amazon.com’s web page to the server
Server responds, also using TCP
Port number identifies the process at the TCP level
Layering!
TCP Connection
Request
TCP Connection
Response
Get
http://www.amazon.com
File in
pieces
Application
(Process)
TCP
Socket

## Slide 41: Network Protocols
They are protocols needed for network components to interact and enable information flows
Protocols define format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Circuit Switching
  Signaling protocols to set up/tear down circuit (e.g., SS7)
Packet Switching
  Protocols to control flow of information (e.g., TCP)

## Slide 42: Layering in Network Protocols
Networks make extensive use of layering of technology and protocols
  Protocols are most often placed in layers
Layering is arranging functionality in a hierarchical manner, such that
  Lower layers provide functions and services that support the functions and services of higher layers
Protocol layers are implemented in hardware or software
  Some are implemented in the operating system kernel (e.g., TCP and IP)
  Physical and link layers are implemented in hardware or firmware

## Slide 43: Advantages of layering
Well defined and specified
  Modularity reduces complexity of implementation
Specializes technology development
Separation of functionality
  Simplification in upgrades
  Example: Change from IPv4 to IPv6 does not require change in email clients or browsers
Simplification in adding new technology
  Adding wireless network capability does not require change in web site addresses (URLs)
Slide modified from Agrawal

## Slide 44: Next class
More about layering and the protocol layers
The OSI and TCP/IP protocol stack models
Trying to understand how the “browsing Amazon.com” works in the context of protocol layers