## Slide 1: Lecture 3a
The Physical Layer (I): Transmission Media

## Slide 2: So far …
Three scenarios
Circuit Vs Packet switching
Protocol stack
Layers
  OSI and Internet

## Slide 3: Starting Today: The PHY Layer
Definition: Provide transparent transmission of a bit stream over a circuit built from some physical communications medium
ATIS Telecom glossary
  http://www.atis.org/glossary/default.aspx
  Earlier versions
    Federal Standard 1037C
      http://www.its.bldrdoc.gov/fs-1037
    ANS T1.523-2001, Telecom Glossary 2000
      http://www.atis.org/tg2k/
Slide modified from Agrawal
ATIS = Alliance for Telecommunications Industry Solutions

## Slide 4
Slide modified from Agrawal
CHAPTER 2
(more details than there)

## Slide 5: Position in the Protocol Stack
Slide modified from Agrawal
Other PHY layers such as optical fiber, wireless
Voltage

## Slide 6: Context
What is involved in getting information from A to B?
  Media – what are different common transmission media?
  Signals – what is a signal?
  Bunch of other stuff (standards, protocols, etc.) to be discussed later
A
B
Signal
Media

## Slide 7: Special feature of the Physical Layer
Physical layer interacts with nature
  Layer where we are at the mercy of nature
  Depend upon wires, optical fibers or air to transmit signals
Signal transmitting properties of chosen media are important
  Signals generated by physical layer comply with properties of the medium
    Examples: voltages with copper, light with fiber, electromagnetic radiation (radio frequency or RF signals)
Slide modified from Agrawal

## Slide 8: Physical media and their properties
The physical medium is the transmission path along which a signal propagates
  Examples: a wire pair, coaxial cable, optical fiber, radio path
Media are chosen for their special properties that enable efficient transmission (movement) of signals
  Example: most plastics cannot be used as physical media because they do not efficiently conduct electricity, light, heat or other forms of energy
  Common media are copper wire, optical fiber, and air
Slide modified from Agrawal

## Slide 9: Copper wire as physical medium
Copper is a very good conductor of electricity and is relatively abundantly available
In computer networking
  8 individual strands of copper wire are organized as four pairs
    This is called Unshielded twisted-pair (UTP)
Each pair of wires is twisted around each other
  Twisting reduces interference from induction
  Tighter twisting improves data rates (reduces noise)
Cat 3 cable
Cat 5 cable
Slide modified from Agrawal

## Slide 10: Categories of UTP cables
Categories range from Cat-1 to Cat-6
  The higher the category, the higher the maximum possible data rate
    And generally more twists-per-inch
  http://en.wikipedia.org/wiki/Category_5_cable
Cable type | Max data rate
Cat 3 | 10 Mbps
Cat 5e | 1,000 Mbps = 1Gbps
Cat 6 | 10 Gbps
Unshielded Twisted Pair
Shield
Shielded Twisted Pair
Slide modified from Agrawal

## Slide 11: UTP and STP Again
Electromagnetic energy passes through an insulator, but is stopped by metal. Thus STP is/has:
  Lower noise susceptibility than UTP
  Lower electromagnetic emissions than UTP
  More expensive than UTP
Figure Source: The Physical Layer of Communication Systems, by R.A. Thompson and Others

## Slide 12: The Variety of Ethernet Physical Layer Standards
Notes: The term Ethernet refers to an entire family of standards Some standards define the specifics of how to send data over a particular type of cabling, and at a particular speed. Other standards define protocols, or rules, that the Ethernet nodes must follow to be a part of an Ethernet LAN. All these Ethernet standards come from the IEEE and include the number 802.3 as the beginning part of the standard name.
Ethernet supports a large variety of options for physical Ethernet links given its long history over the last 40 or so years. Today, Ethernet includes many standards for different kinds of optical and copper cabling, and for speeds from 10 megabits per second (Mbps) up to 100 gigabits per second (Gbps). The standards also differ as far as the types of cabling and the allowed length of the cabling.
T stands for UTP, X stands for biger

## Slide 13: Transmitting data using twisted pairs
Transmitter
Receiver
Notes: While it is true that Ethernet sends data over UTP cables, the physical means to send the data uses electricity that flows over the wires inside the UTP cable. To better understand how Ethernet sends data using electricity, break the idea down into two parts: how to create an electrical circuit and then how to make that electrical signal communicate 1s and 0s.
First, to create one electrical circuit, Ethernet defines how to use the two wires inside a single twisted pair of wires. The figure does not show a UTP cable between two nodes, but instead shows two individual wires that are inside the UTP cable. An electrical circuit requires a complete loop, so the two nodes, using circuitry on their Ethernet ports, connect the wires in one pair to complete a loop, allowing electricity to flow.
To send data, the two devices follow some rules called an encoding scheme.
Note that in an actual UTP cable, the wires will be twisted together, instead of being parallel as shown in figure. The twisting helps solve some important physical transmission issues, like interference.

## Slide 14: Cable connectors
Cat5e cables end in RJ 45 connectors for Ethernet
Not all pairs used in all cases
Some pairs are used for carrying DC power
Conductor identification | Color code | Use
Pair 1 | White-Blue/ Blue | -
Pair 2 | White-Orange/ Orange | Transmit data
Pair 3 | White-Green/ Green | Receive data
Pair 4 | White-Brown/ Brown | -
Slide modified from Agrawal
Notes: To learn about how a UTP Ethernet link works, it helps to break down the physical link into those basic pieces, as shown in figure, the cable itself, the connectors on the ends of the cable, and the matching ports on the devices into which the connectors will be inserted.
First, think about the UTP cable itself. The cable holds some copper wires, grouped as twisted pairs. The 10BASE-T and 100 BASE-T standards require two pairs of wires, while the 1000BASE-T standard requires four pairs. Each wire has a color-coded plastic coating, with the wires in a pair having a color scheme. For example, for the blue wire pair, one wire’s coating is all blud, while the other wire’s coating is blue-and-white striped.
Many Ethernet UTP cables use an RJ-45 connector on both ends. The RJ-45 connector has eight physical locations into which the eight wires in the cable can be inserted, called pin positions, or simply pins. These pins create a place where the ends of the copper wires can touch the electronics inside the nodes at the end of the physical link so that electricity can flow.
To complete the physical link, the nodes each need an RJ-45 Ethernet port that matches the RJ-45 connectors on the cable so that the connectors on the ends of the cable can connect to each node. PCs often include this RJ-45 Ethernet port as part of a network interface card (NIC), which can be an expansion card on the PC or can be built in to the system itself. Switches typically have many RJ-45 ports because switches give user devices a place to connect to the Ethernet LAN.

## Slide 15: UTP Cabling Pinouts for 10BASE-T and 100 BASE-T
Straight-Through Cable Pinout
Cross-over cable
Notes: Straight-through cable: 10BASE-T and 100BASE-T use two pairs of wires in a UTP cable, one for each direction, as shown in figure. The figure shows four wires, all of which sit inside a single UTP cable that connects a PC and a LAN hub. In this example, the PC on the left transmits using the top pair, and the hub on the right transmits using the bottom pair. For correct transmission over the link, the wires in the UTP cable must be connected to the correct pin positions in the RJ-45 connectors. For example, in figure, the transmitter on the PC on the left must know the pin positions of the two wires it should use to transmit. Those two wires must be connected to the correct pins in the RJ-45 connector on the hub, so that the hub’s receiver logic can use the correct wires.
To understand the wiring of the cable-which wires need to be in which pin positions on both ends of the cable-you need to first understand how the NICs and hubs work. As a rule, Ethernet NIC transmitters use the pair connected to pins 1 and 2; the NIC receivers use a pair of wires at pin positions 3 and 6. LAN hubs, knowing those facts about what Ethernet NICs do, do the opposite: Their receivers use the wire pair at pins 1 and 2, and their transmitters use the wire pair at pins 3 and 6.
To allow a PC NIC to communicate with a hub, the UTP cable must also use a straight-through cable pinout. The term poinout refers to the wiring of which color wire is placed in each of the eight numbered pin positions in the RJ-45 connector. An Ethernet straight-through cable connects the wire at pin 1 on one end of the cable to pin 1 at the other end of the cable; the wire at pin 2 needs to connect to pin 2 on the other end of the cable; pin 3 on one end connects to pin 3 on the other, and so on. Also, it uses the wires in one wire pair at pins 1 and 2, and another pair at pins 3 and 6.
Crossover cable pinouts: A straight-through cable works correctly when the nodes use opposite pairs for transmitting data. However, when two like devices connect to an Ethernet link, they both transmit on the same pins. In that case, you then need another type of cabling pinout called a crossover cable. The crossover cable pinout crosses the pair at the transmit pins on each device to the receive pins on the opposite device. The figure whos what happens on the link between two PCs. The two PCs both transmit on the pair at pin 1 and 2, and they both receive on the pair at pins 3 and 6. So, the cable must connect a pair at pins 1 and 2 on each side to pins 3 and 6 on the other side, connecting to the other node’s receiver logic.

## Slide 16: UTP Cabling Pinouts for 10BASE-T and 100 BASE-T

## Slide 17: UTP Cabling Pinouts for 10BASE-T and 100 BASE-T
Questions: which cable you should use, straight-through cable or crossover cable when
  Connect PC to PC
  Connect PC to Switch
  Connect Switch to Switch

## Slide 18: UTP Cabling Pinouts for 10BASE-T and 100 BASE-T

## Slide 19: Coaxial cable
Applications
  Ethernet (until circa 1987)
  Cable TV
  IBM terminal connections
Good propagation characteristics
Larger bandwidth
Can be unwieldy to manage
Flexible
Inner strands
Semi rigid
Figure Source: The Physical Layer of Communication Systems, by R.A. Thompson and Others

## Slide 20: Copper is Used Almost Everywhere
Example: USB SuperSpeed
  Notice wire for power
  Notice how many wires are squeezed in the cable
  5 Gbps
Short length!
Source: SuperSpeed USB PHY Layer Specification
Presentation by Howard Heck, Intel

## Slide 21: Why not copper?
Great for short distances
  Local networking or communications! (where the word LAN comes from)
  Attenuation and loss (to be visited) requiring repeaters
    Noise may add up
  Long haul networks use optical fiber
Data rates are limited
  10 Gbps or so
Weight and so cost of installation
Needs mining – compare with glass
  More robust
http://1800recycling.com/wp-content/uploads/2013/04/Earth-Day-hands.jpg

## Slide 22: Optical fiber as physical medium
Optical fiber is a thin strand of glass that guides light along its length
  Can carry large volumes of data over long distances
  Larger pipe – two lane Versus four lane highway
Typically aggregate traffic is carried over fiber in long-haul links
Local networks are also using optical fiber
  FiOS = Fiber To The Home (FTTH) or Fiber to the Premises (FTTP)
    Optical Fiber is now in the access network
Slide modified from Agrawal

## Slide 23: Submarine optical fiber installation
Slide modified from Agrawal
Reliability?
http://www.submarinecablemap.com

## Slide 24: Optical fiber as Physical medium
Glass is a good conductor of light
  Not heavy and made from sand, which is abundantly available
Works on the principle of Total Internal Reflection
  Light can escape only if it hits the wall at right angles
  Since there is little energy loss, fiber can transmit signals over huge distances without repeaters
Slide modified from Agrawal
(rare)
(dense)

## Slide 25: Principle of Operation of Optical Fibers
Lower Refraction Index
Higher Refraction Index
Reflected Light
Incident Light
Refracted
Light
Normal Refraction
Lower Refraction Index
Higher Refraction Index
Reflected Light
Incident Light
Total Internal
Reflection
Notes: This refractive index works with any boundary, such as glass and water as well.

## Slide 26: Characteristics of Optical Fibers
Uses light impulses instead of electrical signals
Properties and characteristics
  Very high bandwidth
  Very high noise immunity
Much less susceptible to noise, but subject to signal dispersion that results in intersymbol interference

## Slide 27: Types of optical fiber
Multiple mode
  50 - 100 microns in diameter
  Uses LED as light source (less expensive)
  Can transmit data over short-to-medium distances
  Used on short links (upto about 2000 m)
Single mode
  About 10 microns in diameter
  Uses Laser light source
  Can transmit data over very long distances
  Used on trunk routes
Slide modified from Agrawal
1 micron = 1 μm = 10-6 m

## Slide 28: Construction of optical fiber
Core has high refractive index
Cladding has low refractive index
Together, they keep light inside the optical fiber
Slide modified from Agrawal

## Slide 29: Wireless
Provides “tether-free” communications
  Convenience, mobility
Wireless communication system
  Any communication system that uses a naturally occurring communication medium, such as air, water, earth.
Examples:
  Cell phone, sonar, ground penetrating radar
  Broadcast: (one way)
    Radio, TV, pagers, satellite TV
  Two Way:
    Walkie talkie, cell phones, satellite phones, WiFi, Bluetooth
Fundamentally different from wired networks
NOT PHYSICAL, yet physical layer

## Slide 30: Radio Spectrum
One part of Electromagnetic Waves.
When electrons move, they create electromagnetic waves that can propagate through space (even in vacuum).

## Slide 32: Radio Spectrum

## Slide 33: Electromagnetic wave
Frequency: the number of oscillations per second of a wave, measured in Hz
Wavelength: distance between two consecutive maxima
Wavelength = c/f

## Slide 34: Narrow vs Broadband
Most transmission use a relatively narrow frequency band.
However, in some cases, a wider band is used:
  Frequency hopping spread spectrum
  Direct sequence spread spectrum (CDMA)
  Ultra Wide Band

## Slide 35: Mobile Vs. Wireless
Mobile and Wireless are not interchangeable
Mobile and wireless communication systems
  Communicate over the air via radio-waves
  Support some form of user mobility
Mobile | Wireless | Example
 |  | Desktop computer with Ethernet, pay phone
 |  | Wireless local loop
 |  | Calling card, call forwarding
 |  | Cell phone, laptop with WLAN

## Slide 36: Transmission Medium = Air
It is hard, if not impossible to slice wireless transmissions in “space”
  New technologies like MIMO try to do some of this
The common way of slicing spectrum is to “allocate” different frequency bands to different applications and service providers over different geographical areas
Power, frequency bands, applications, receiver capability, all impact wireless
Typically uses electromagnetic radiation, not light impulses or electrical voltages/currents for communication

## Slide 37: Spectrum allocation
The Federal Communications Commission (FCC) regulates spectrum in the US
  Licensed Vs Unlicensed
Auctions
  Minimum bid in UK for one piece (30 MHz) of spectrum was 125 million pounds

## Slide 38: Wired Vs. Wireless Example
Wireless has much different behavior and issues compared to wired networks
LAN Design
  Selection of technology (e.g., 100 Mbps, 1 Gbps, 10Gbps Ethernet) and cabling (e.g., coax, twisted pair, optical; plenum vs. nonplenum).
WLAN Design selection of technology (e.g., 802.11 a/b/g/n/ac) and AP Placement based on
    Signal coverage and capacity
    Power level and access to AC power
    Frequency channel selection
    Connection to wired infrastructure
  Take measurements to get signal quality map
-80 dBm
-80 dBm

## Slide 39: Wireless also needs Antennas
  A transducer for converting guided signals in a transmission line or waveguide into electromagnetic radiation in an unbounded medium or vice versa
Any conductor or dielectric can serve as the transducer <link> (http://www.oreillynet.com/cs/weblog/view/wlg/448)
  The properties may make it inefficient and thus unsuitable for the application
Thin Dipole
Biconical Dipole
Loop
Parabolic
Reflector
Microstrip
Horn
Antenna

## Slide 40: Key Takeaways – transmission media
Cable type | Cost | Ease of use | Capacity | Noise Susceptibility | EM radiation (interference)
Twisted pair | Low | High | Low | High | High
Coax | Medium | Medium | Good | Lower | Lower
Multimode Fiber | Medium | Medium | High | Very low | Almost zero
Single mode fiber | Highest | Lowest | Highest | Very low | Almost zero
Wireless | Variable | Variable | Low | High | High

## Slide 41: Next class
Signals, bandwidth, and other physical layer issues
Please install {R-studio and R} or Matlab on your computers