## Slide 1: Lecture 3b
The Physical Layer (2): Signals

## Slide 2: Information Vs. Data
Information depends on “uncertainty” and “surprise”
Consider
  The sun is rising in the east
  I see a herd of elk near my house
  I see a red dragon
Which has the most surprise?
Which has the most information?

## Slide 3: Mind Reading Vs. Speaking
Your thoughts are “encoded” into words
Words are carried by audio signals
  Mouth = Transmitter (Tx)
  Ear = Receiver (Rx)
http://static.ddmcdn.com/gif/mind-reading-120131-676450-.jpg

## Slide 4: Speaking (Audio Signal)
Alice
Bob
It is sublime
http://indianapublicmedia.org/amomentofscience/files/2009/07/3705-940x626.jpg
http://amotherworld.com/main/wp-content/uploads/2010/11/kids.jpg
So grand, it is inspiring me
She says it is impressive…
Did she want a subway sandwich?

## Slide 5: Information -> Data -> Moving Data
How can we move information from one location to another (assuming a channel exists)?
Data
  Encoding of information (digital or analog?)
  Representation of facts in a formalized manner suitable for communication, interpretation, or processing by humans or by automatic means
  Example: Word document or numbers in computer spreadsheets
How do we move data from one location to another (assuming a channel exists)?
What are the properties and impairments associated with these techniques?
Slide modified from Agrawal

## Slide 6: Historical Strategies
Physical
  Mail
  Carrier pigeons
  Touch
Acoustic
  Speech
  African drums
Optical
  Smoke signals
  Semaphore tower chains
http://upload.wikimedia.org/wikipedia/commons/9/94/OptischerTelegraf.jpg

## Slide 7: Signals
Signal
  Detectable transmitted energy that can be used to carry data or
  A time-dependent variation of a characteristic of a physical phenomenon, used to convey data
  Example: voice in humans or wire voltage in computer networks
Electrical or optical energy, RF waves
We will focus on electrical energy, maybe RF waves
  Typically a voltage on a wire
  Must be changing over time to carry information
Slide modified from Agrawal

## Slide 8: Signals (2)
Mathematically, a signal is represented as a function of time – or can be expressed as a function of frequency
  Example: s(t) or S(f)
Communication systems perform the tasks of
  Signal generation (conversion of information to signal)
  Signal transmission
  Signal reception
  Signal detection (conversion of signal to information)

## Slide 9: Simple Tx-Rx-Channel
The source produces a signal in time – s(t)
  Example: When we speak, an audio signal is created
  Example: When we speak into a microphone, the audio vibrations are converted into an electrical signal
The channel carries the signal to the sink (for now, transmission medium)
  Example: Air carries audio to ear
Noise – n(t) – is a signal that distorts s(t)

## Slide 10: Signals and their properties
Signals are changes in energy that can be detected at the receiver
Good signals can provide
  Easy detection by receiver (simply tune in)
  Immunity from noise (compare FM vs. AM)
  Efficient use of bandwidth
  Multiplexing
    Combine many signals at sending end and separate them at the receiving end
Slide modified from Agrawal

## Slide 11: Impacts of improved signaling
Slide modified from Agrawal
See http://www.a-bc.co.uk/dab.html
Easy reception
  CDMA signals are much easier to detect than older analog signals
  Modern cell phones require less transmission power to send detectable signals, and can be smaller in size
Noise resistance
  FM has much better noise resistance than AM
  Hi-fi music transmission is possible over broadcast radio using FM
http://upload.wikimedia.org/wikipedia/commons/thumb/7/74/DynaTAC8000X.jpg/220px-DynaTAC8000X.jpg

## Slide 12: Impacts of improved signaling (2)
Efficient utilization of bandwidth
  Data compression and improved signaling allow eight hi-definition TV channels to be transmitted using the same bandwidth as one traditional analog TV channel
  The remaining bandwidth is being auctioned for cell-phone usage
Multiplexing
  Radio, TV, cell phones, fire, police, wi-fi and other users can easily transmit signals over the same medium (air)
Slide modified from Agrawal

## Slide 13: Categories of signals
All signals involve creating change at the sending end that can be detected at the receiving end
Common approaches
  Turn a switch on or off depending upon whether data to send is 0 or 1 (digital signal)
  Create a sine wave and change (modulate) its amplitude or frequency, hence the names AM and FM (analog signal)
Slide modified from Agrawal
Analog Signal

## Slide 14: Analog Signals
Continuous variation in time
Information is contained in each absolute signal level at each point in time
Time (seconds)
Amplitude(volts)

## Slide 15: Digital signals
The amplitude values take on a finite set of values
  Information is contained in discrete, well defined levels
  Two-levels => binary
  Multiple levels
    M-Ary for M levels
    Still carry bits!
Time (seconds)
Amplitude(volts)

## Slide 16: Periodic and Aperiodic Signals
Periodic: pattern repeated over time (e.g., sine wave)
Aperiodic: no repeated pattern to the signal
Notes: We have to characterize signals so that we can determine their properties. This can be done analytically, but we will take a qualitative approach. The analytical characterization of signals will be covered in Telcom 2060.
Characterizing the signal allows us to consider the ability of signals to carry information under a variety of circumstances. You will recall that different cable types had different susceptibilities: UTP had high attenuation and noise susceptibility, both of which were reduced by STP, coax, and, finally, optical fibers.

## Slide 17: Sinusoids (1)
Sinusoids are periodic
The idea of “frequency” is easiest with sinusoids
Typical form: s(t) = Acos(2πfct + φ)
What is the frequency?

## Slide 18: Sinusoids (2)
Frequency (fc)
  Number of repetitions per second (unit is hertz): 5 KHz  5000 times per second
Period (T) - amount of time it takes for one repetition of the signal
  T = 1/frequency = 1/f 5KHz  T = .2 ms
Phase () - measure of the relative position in time within a single period of the signal
Wavelength () - distance occupied by a single cycle of the signal
  For electromagnetic waves in air  = c/f where c is the speed of light = 3 x 108 m/sec

## Slide 19: Some Sinusoids

## Slide 20: Some Trigonometric Identities
What is cos 2A?
What is cos 0?
What is sin 2A

## Slide 21: Why sinusoids and trigonometry?
Any periodic signal can be broken into a sum of weighted sinusoids
The frequency f0 is called the “fundamental” frequency
  Multiples of f0 are called “harmonics”
We only need the “weights” Cn to get the actual signal (discrete)
  Think of the weights as “how much energy is there at that frequency”
Fourier Series

## Slide 22: Example
Bandwidth

## Slide 23: Clarinet and Violin
The violin and clarinet play the same note A sinusoid at the note’s fundamental frequency f0 For example, f0 = 440 Hz for “middle A”
Both the violin and clarinet would sound identical like a tuning fork, but they don’t!
Clarinet’s tube and violin’s string add harmonics Infinite number of harmonics – but weights Cn are different
Similarly, human voice and speech have distinguishing weights

## Slide 24: Aperiodic Signals
They have a continuous range of frequencies in them
  No longer just the harmonics
A fat aperiodic signal has a smaller range of frequency content
A thin aperiodic signal has a larger range of frequency content
time
time
frequency
frequency
Bandwidth
Bandwidth

## Slide 25: Bandwidth
Measure of the range of frequencies in a signal Half-power bandwidth
  Interval where spectrum falls to ½ the maximum value
Null-to-null bandwidth - Width of the mainlobe of the spectrum
Fractional containment bandwidth - Width of the spectrum that contains 95% or 99% of the power (FCC)
Out-of band emission level - Width of spectrum beyond which the spectrum value is some dB below the maximum

## Slide 26: Spectrum and Bandwidth
Spectrum – a range/continuum of frequencies.
  Radio Spectrum 0 – 300 GHz
  Visible Spectrum 400 – 790 THz
Band – a small slice of the spectrum
  USA AM Radio band 530-1710 kHz
Absolute bandwidth - width of the spectrum of a signal
Effective bandwidth (bandwidth) - band of frequencies that contains most of the signal’s energy
  Example: human voice – absolute bandwidth 0-20 kHz, effective bandwidth 50 – 3400 Hz.

## Slide 27: Frequency and Time
A signal can be represented in frequency or in time
If we look at frequency, we call it the “spectrum” of the signal
  This is a loose and simplified definition
Signals can “interfere” in time or in frequency
  What if the kids started shouting at a different time?
  How about an ultrasonic dog whistle?

## Slide 28: Filters
Filters allow certain frequencies to go through and stop other frequencies
  Useful for separating multiplexed signals
The attenuation and phase of different frequencies can be affected differently
Channels (transmission media) are often like filters

## Slide 29: Types of Ideal Filters

## Slide 30: Key Takeaways
The frequency domain representation helps us understand bandwidth more precisely
The bandwidth of a signal consists of its frequency range
Signals with shorter periods (or thin in time) have greater bandwidth than signals with longer periods (or fat in time)
Later
  Different digital signals (line codes) have different bandwidths